## Slide 1: CE 413 Structural Analysis & Design III
Md. Abu Hasan
Senior Lecturer
Department of Civil Engineering
Daffodil International University.
Concrete Filled Tube (CFT)
Composite Column

## Slide 2: Concrete Filled Tube Column (CFT)
CONCRETE FILLED TUBULAR COLUMNS (CFT/HSS)
Steel shell ( pipe, tube, or hollow section built-up from plate)
Shell provides formwork for concrete
Shell provides confinement to concrete

## Slide 3: Concrete Filled Tube Column (CFT)
CONCRETE FILLED TUBULAR COLUMNS (CFT/HSS)
Concrete adds strength, stiffness
Might use when exposed steel is desired
Steel can buckle outwards
Shear connectors might be needed near beam-to-column connections

## Slide 4: Concrete Filled Tube Column (CFT)
BEHAVIOUR OF CFT COLUMNS
Flexural stiffness governed by steel shell
Initial compressive strain – steel expands more than concrete, causes micro cracking
Expansion of concrete then restrained by steel
Steel reaches yield, inelastic outward buckling may occur, concrete crushes

## Slide 5: Concrete Filled Tube Column (CFT)
BEHAVIOUR OF CFT COLUMNS
CONFINEMENT
Confinement from steel shell can increase effective strength of concrete However, stiffness reduced by
micro cracking.

## Slide 6: Concrete Filled Tube Column (CFT)
AISC DESIGN PROVISIONS
AISC Limitations
To qualify as a composite column :
3 ksi ≤ f ‘c ≤ 10 ksi (Normal weight)
3 ksi ≤ f ‘c ≤ 6 ksi (Light weight)
As ≥ 0.01
Ag
Concrete strength : Super column 12 ksi

## Slide 7: Concrete Filled Tube Column (CFT)
AISC DESIGN PROVISIONS
AISC Limitations, cont’d
Steel strength (used in calculations) :
Fy and Fyr ≤ 75 ksi
Corresponds roughly to 0.003 strain limit for concrete

## Slide 8: Concrete Filled Tube Column (CFT)
AISC DESIGN PROVISIONS
Local Buckling of CFT sections
λp for Axial Compression
b ≤ 2.26 √ E t Fy
D ≤ 0.15 E t Fy
t
b
D
t

## Slide 9: Concrete Filled Tube Column (CFT)
b is for longer side / dimension
t = design wall thickness (0.93 * nominal
wall thickness (AISC B 4.2))
AISC B4.1 b = clear distance between webs less inside corner radius
Radius not know?
Use b = w – 3t
AISC DESIGN PROVISIONS
Local Buckling of CFT sections
t
b
w

## Slide 10: Concrete Filled Tube Column (CFT)
AISC DESIGN PROVISIONS
Fig . C.I2.1. Changes in cross sectional buckling mode due to concrete infill.
Change Steel Wall
Buckling Steel Wall
Concrete infill
Change Steel Wall
Change Buckling
Steel Wall
Change Buckling Steel Wall
Change Steel Wall
Fig . C.I1.3. Changes in buckling mode with length due to the presence of infill.

## Slide 11: Concrete Filled Tube Column (CFT)
TABLE I1.1A Limiting Width-to-Thickness Ratios for Compression Steel Elements in Composite Members Subject to Axial Compression For Use with Section I2.2 |  |  |  | 
Description of Element | Width-to- Thickness Ratio | λp Compact / Noncompact | λr Noncompact / Slender | Maximum Permitted
Walls of Rectangular HSS and Boxes of Uniform Thickness | b/t | 2.26 √ E Fy | 3.00 √ E Fy | 5.00 √ E Fy
Round HSS | D/t | 0.15E Fy | 0.19E Fy | 0.31E Fy
AISC DESIGN PROVISIONS

## Slide 12: Concrete Filled Tube Column (CFT)
TABLE I1.1B Limiting Width-to-Thickness Ratios for Compression Steel Elements in Composite Members Subject to Flexure For Use with Section I3.4 |  |  |  | 
Description of Element | Width-to- Thickness Ratio | λp Compact / Noncompact | λr Noncompact / Slender | Maximum Permitted
Flanges of Rectangular HSS and Boxes of Uniform Thickness | b/t | 2.26 √ E Fy | 3.00 √ E Fy | 5.00 √ E Fy
Webs of Rectangular HSS and Boxes of Uniform Thickness | h/t | 3.00 √ E Fy | 5.70 √ E Fy | 5.70 √ E Fy
Round HSS | D/t | 0.09E Fy | 0.31E Fy | 0.31E Fy

## Slide 13: Concrete Filled Tube Column (CFT)
AISC DESIGN PROVISIONS
Pno = Pp -
Pp – Py
( λr – λp) 2
( λ – λp)2
λr Max
Nominal Section Strength, Pno
Pp Py
λp
Tube Slenderness
Limits per Table I 1.4 (a), b/t or D/t
Fig . C.I2.1. Nominal axial strength, Pno vs. HSS slenderness
𝐸𝑐
𝐸𝑠
Pno = As Fcr + 0.7 f’c ( Ac – Asr )

## Slide 14: Concrete Filled Tube Column (CFT)
COMPRESSIVE STRENGTH OF CFT COLUMNS
The available compressive strength of axially loaded doubly symmetric filled composite members shall be determined for the limit state of flexural buckling.
(b) For Compact Sections
Pno = Pp
Where
Pp = FyA
s + C2f‘c (Ac + Asr )
C2 = 0.85 for rectangular sections and 0.95 for round sections
Es
Ec

## Slide 15: Concrete Filled Tube Column (CFT)
COMPRESSIVE STRENGTH OF CFT COLUMNS
(b) For Noncompact Sections
Where
Pp - Pp
Pno = Pp -
( λr – λp)
( λ – λp)
2
2
λ, λp and λr are slenderness ratios determined from Table I1.1a
Pp is determined from Equation I2-9b
Py = FyAs + 0.7f‘c (Ac + Asr Es )
Ec

## Slide 16
Concrete Filled Tube Column (CFT)
COMPRESSIVE STRENGTH OF CFT COLUMNS
(c) For Slender Sections
Where
(i) For rectangular filled sections
Fcr =
9Es
b
2
Pno = Fcr As + 0.7f‘c (Ac + Asr Es )
Ec
t
( )
(ii) For round filled sections
Fcr =
0.72Fy
D
0.2
t
Fy
Es
(( )
)

## Slide 17: Concrete Filled Tube Column (CFT)
The available compressive strength need not be less than specified for the bare steel
member as required by Chapter E.
COMPRESSIVE STRENGTH OF CFT COLUMNS
The effective stiffness of the composite section, EIeff , for all sections
EIeff = EsIs + EsIsr + C3EcIc
Where
C3 = Coefficient for calculation of effective rigidity of filled composite
compression member
= 0.6+2 [ ] ≤ 0.9
As
Ac +As

## Slide 18: Concrete Filled Tube Column (CFT)
COMPRESSIVE STRENGTH OF CFT COLUMNS
Elastic Buckling Strength
Pe
= π2 EIeff
( KL )2
EIeff = Effective rigidity of composite section
K = Effective length factor
L = Laterally unbraced length of the member (in)

## Slide 19
Concrete Filled Tube Column (CFT)
COMPRESSIVE STRENGTH OF CFT COLUMNS
Nominal Compressive Strength
> 2.25
If …. Pno ≤ 2.25
Pe
Pno
Pe
( )
]
Pn = Pno [0.658
Else …. Pno
Pe
Pn = 0.877 Pe
The design compressive strength = Φc Pn
Allowable compressive strength = Pn / Ωc
Φc = 0.75 (LRFD)
Ωc = 2.00 (ASD)

## Slide 20: Concrete Filled Tube Column (CFT)
TENSILE STRENGTH OF CFT COLUMNS
Tensile Strength
The design tensile strength , Φt Pn , and allowable tensile strength, Pn / Ωt , for filled composite columns shall be determined for the limit state of yielding as :
Pn = As Fy + Asr Fyr
Φt = 0.90 (LRFD) Ωt = 1.67 (ASD)

## Slide 21: Concrete Filled Tube Column (CFT)
Fully encased composite (FEC) Columns
Partially Encased Composite (PEC) Columns
Concrete Filled Tubes / Hollow Structural Sections

## Slide 22: J. M. Raisul Islam Shohag, Lecturer, Department of Civil Engineering, DIU