## Slide 1: CE 413 Structural Analysis & Design III
Md. Abu Hasan
Senior Lecturer
Department of Civil Engineering
Daffodil International University.
Design of Partially Encased Composite Column

## Slide 2: Design of PEC Column
d=400 mm
b = 200 mm bf = 400 mm
Problem-1 :
Check whether this provided PEC section satisfies the code specified limits for geometric and material properties .
Given , f’c = 30 Mpa , fy = 350 Mpa
Link 12 mm @250 mm c/c
38 mm cover
t = 7mm

## Slide 3: Design of PFC Column
Solution:
Material limitations:
1 ) Concrete strength : 21 Mpa ≤ f’c
≤ 70 Mpa
Here, f’c = 30 Mpa ok
2 ) Structural steel : Fy ≤ 350 Mpa . Here , Fy = 350 Mpa Here, Fy = 350 Mpa ok
Reinforcement Limit:
As + Asr ≤ 20% of gross cross sectional area. As= 7*400*2+ (400-7*2)*7= 8302 𝑚𝑚2 Ar= 0
Ag= 400*400 =160000 𝑚𝑚2
As + Ar /Ag = (8302 + 0/160000)*100 = 5.2% <20% ok

## Slide 4: Design of PEC Column
ok
b/t = 200/7 = 28.6 < 32 ok
Link bar limitations:
500 mm
S ≤ 2/3 d = 2/3 *400 = 266.7 mm 2/3 bf = 2/3 *400 = 266.7 mm
Here, spacing = 250mm < 266.7 mm, Taken 250 mm
63 𝑚𝑚2
Area of a tie bar, Atie >_
0.01 bf t = 0.01*400*7 = 28 𝑚𝑚2
0.5 𝑚𝑚2 * s = 0.5 *250 = 125 𝑚𝑚2
Solution:
Geometric Limit:
bf should be between 0.9 d to 1.1 d
Here bf = 1.1 d = 440 mm & 0.9 x 400 = 360 mm
Taken
125
𝑚𝑚2

## Slide 5: Design of PEC Column
п∗122
4
=113 𝑚𝑚2 ˂ 125 𝑚𝑚2 (not ok)
Tie bar cover ≥ 30 mm
Here, cover = 38mm > 30 mm (ok)
Solution:
Here, Area of tie bar =

## Slide 6: Design of PEC Column
d=400 mm
b = 200 mm bf = 400 mm
Problem-2 :
Determine the axial capacity of PEC column section. Given , f’c = 30 Mpa , fy = 350 Mpa
Link 12 mm @250 mm c/c
38 mm cover
t = 7mm

## Slide 7: Design of PEC Column
Axial Compressive Strength:
Pr = Ase Fy + 0.85 f’cﹶ Ac + Asr Fyr
Here,
Ase = (d - 2t + 2be)* t
To calculate the value of be complete these following steps
⸫
𝑠
𝑏𝑓
400
= 250 = 0.625,
⸫ 0.5 <
𝑠
𝑏𝑓
< 1 (ok)
Now, λp = t √(
𝑏 12∗ 1−ω𝑠2
∗ 𝐹𝑦
200000∗п2∗𝑘
)
7
200000∗п2∗𝑘
2
= 200 √(12∗ 1−0.3 ∗350)
hear, ωs = 0.3
Solution:
Es = 200 Gpa = 200000 MPa

## Slide 8: Design of PEC Column
Here, k =
0.9
(s / bf)2
+ 0.2 (s/bf)2 + 0.75
= 3.13
λp =
200 12∗ 1−0.32 ∗350
*√( )
7 200000∗п2∗3.1
=0.714
Now, be =
𝑏𝑓 (1+λp2𝑛)1/𝑛
=
400
(1+0.7142∗1.5)1/1.5
= 325.2 ˂ 𝑏𝑓 = 400.
be = 325.2 mm
⸫ Ase = (400-2*7+2*325.2)*7
= 7255 𝑚𝑚2
Solution:

## Slide 9: Design of PEC Column
Solution:
Ac = Ag - As = 400*400 – [(400 - 2*7)*7 + 400*7*2]
= 151698 𝑚𝑚2
⸫Pr = Ase Fy + 0.85 f’c Ac + Asr Fyr
= 7255*350 + 0.85*30*151698 + 0
= 6408 KN (Answer)