## Slide 1: Lecture - Internet Protocol Addresses IPV4 Addressing
Professor Dr. A.K.M Fazlul Haque
Department of Electronics and Telecommunication
Engineering (ETE)
Daffodil International University

## Slide 2: IP Address Classes
IP addresses are divided into 5 classes, each of which is designated with the alphabetic letters A to E.
Class D addresses are used for multicasting.
Class E addresses are reserved for testing & some mysterious future use.

## Slide 3: IP Address Classes (Cont.)
The 5 IP classes are split up based on the value in the 1st octet:

## Slide 4: IP Address Classes (Cont.)
Using the ranges, you can determine the class of an address from its 1st octet value.
An address beginning with 120 is a Class A address, 155 is a Class B address & 220 is a Class C address.

## Slide 5: Is This the Host or the Network?
The 32 bits of the IP address are divided into Network & Host portions, with the octets assigned as a part of one or the other.

## Slide 6: Is This the Host or the Network? (Cont.)
Each Network is assigned a network address & every device or interface (such as a router port) on the network is assigned a host address.
There are only 2 specific rules that govern the value of the address.
– A host address cannot be designated by all zeros or all ones.
– These are special addresses that are reserved for special purposes.

## Slide 7: Class A Addresses
Class A IP addresses use the 1st 8 bits (1st Octet) to designate the Network address.
The 1st bit which is always a 0, is used to indicate the address as a Class A address & the remaining 7 bits are used to designate the Network.
The other 3 octets contain the Host address.

## Slide 8: Class A Addresses (Cont.)
There are 128 Class A Network Addresses, but because addresses with all zeros aren’t used & address 127 is a special purpose address, 126 Class A Networks are available.

## Slide 9: Class A Addresses (Cont.)
There are 16,777,214 Host addresses available in a Class A address.
Rather than remembering this number exactly, you can use the following formula to compute the number of hosts available in any of the class addresses, where “n” represents the number of bits in the host portion:
(2n – 2) = Number of available hosts

## Slide 10: Class A Addresses (Cont.)
For a Class A network, there are:
  2^24 – 2 or 16,777,214 hosts.
Half of all IP addresses are Class A addresses.
You can use the same formula to determine the number of Networks in an address class.
Eg., a Class A address uses 7 bits to designate the network, so (2^7 – 2) = 126 or there can be 126 Class A Networks.

## Slide 11: Class B IP Addresses
Class B addresses use the 1st 16 bits (two octets) for the Network address.
The last 2 octets are used for the Host address.
The 1st 2 bit, which are always 10, designate the address as a Class B address & 14 bits are used to designate the Network. This leaves 16 bits (two octets) to designate the Hosts.

## Slide 12: Class B IP Addresses (Cont.)
So how many Class B Networks can there be?
Using our formula, (2^14 – 2), there can be 16,382 Class B Networks & each Network can have (2^16 – 2) Hosts, or 65,534 Hosts.

## Slide 13: Class C IP Addresses
Class C addresses use the 1st 24 bits (three octets) for the Network address & only the last octet for Host addresses .The 1st 3 bits of all class C addresses are set to 110, leaving 21 bits for the Network address, which means there can be 2,097,150 (2^21 – 2) Class C Networks, but only 254 (2^8 – 2) Hosts per Network.

## Slide 14: Class C IP Addresses (Cont.)

## Slide 15: Special Addresses

## Slide 16: Special Addresses (Cont.)
Within each address class is a set of addresses that are set aside for use in local networks sitting behind a firewall or NAT (Network Address Translation) device or Networks not connected to the Internet.

## Slide 17: Subnet Mask
An IP address has 2 parts:
– The Network identification.
– The Host identification.
Frequently, the Network & Host portions of the address need to be separately extracted.
In most cases, if you know the address class, it’s easy to separate the 2 portions.

## Slide 18: Subnet Mask (Cont.)
With the rapid growth of the internet & the ever-increasing demand for new addresses, the standard address class structure has been expanded by borrowing bits from the Host portion to allow for more Networks.
Under this addressing scheme, called Subnetting, separating the Network & Host requires a special process called Subnet Masking.

## Slide 19: Subnet Mask (Cont.)
The subnet masking process was developed to identify & extract the Network part of the address.
A subnet mask, which contains a binary bit pattern of ones & zeros, is applied to an address to determine whether the address is on the local Network.
If it is not, the process of routing it to an outside network begins.

## Slide 20: Subnet Mask (Cont.)
The function of a subnet mask is to determine whether an IP address exists on the local network or whether it must be routed outside the local network.
It is applied to a message’s destination address to extract the network address.
If the extracted network address matches the local network ID, the destination is located on the local network.

## Slide 21: Subnet Mask (Cont.)
However, if they don’t match, the message must be routed outside the local network.
The process used to apply the subnet mask involves Boolean Algebra to filter out nonmatching bits to identify the network address.

## Slide 22: Boolean Algebra
Boolean Algebra is a process that applies binary logic to yield binary results.
Working with subnet masks, you need only 4 basic principles of Boolean Algebra:
–> 1 and 1 = 1
–> 1 and 0 = 0
–> 0 and 1 = 0
–> 0 and 0 = 0

## Slide 23: Boolean Algebra (Cont.)
In another words, the only way you can get a result of a 1 is to combine 1 & 1. Everything else will end up as a 0.
The process of combining binary values with Boolean Algebra is called Anding.

## Slide 24: Default Standard Subnet Masks
There are default standard subnet masks for Class A, B and C addresses:

## Slide 25: A Trial Separation
Subnet masks apply only to Class A, B or C IP addresses.
The subnet mask is like a filter that is applied to a message’s destination IP address.
Its objective is to determine if the local network is the destination network.

## Slide 26: A Trial Separation (Cont.)
The subnet mask goes like this:
1. If a destination IP address is 206.175.162.21, we know that it is a Class C address & that its binary equivalent is:
11001110.10101111.10100010.00010101

## Slide 27: A Trial Separation (Cont.)
2. We also know that the default standard Class C subnet mask is: 255.255.255.0 and that its binary equivalent is:
11111111.11111111.11111111.00000000

## Slide 28: A Trial Separation (Cont.)
3. When these two binary numbers (the IP address & the subnet mask) are combined using Boolean Algebra, the Network ID of the destination network is the result:

## Slide 29: A Trial Separation (Cont.)
4. The result is the IP address of the network which in this case is the same as the local network & means that the message is for a node on the local network.

## Slide 30: Routing IP Addresses
When you build a network, you need to figure out how many network Ids your network requires.
To do so, you must account for every WAN connection & subnet on the Network.
Every node & router interface requires a Host address, or ID.

## Slide 31: Routing IP Addresses (Cont.)
There’s no hard & fast rule on how you should dole out your allotted IP addresses.
Commonly, though, the lowest numbers (1 through 10) are assigned to routers & servers but how you assign addresses is strictly up to you & your network policies & guidelines.

## Slide 32: Configuring an IP Address
The proper way to configure an IP address on the router is through the IP Address command, which assigns each router interface its unique IP address.
A router with 4 interfaces needs 4 separate IP addresses because, technically each interface (& address) is on a different network.