## Slide 1
IO Devices
Zannatul Mawa Koli
Lecturer
Department of CSE
Daffodil International University
Lectute Three

## Slide 2: Learning Objectives
🗌 In this lecture you will learn about:
Input/Output (I/O) devices Commonly used input devices Commonly used output devices
Other concepts related to I/O devices

## Slide 3: I/O Devices
🗌 Provide means of communication between a
computer and outer world
🗌 Also known as peripheral devices because they surround the CPU and memory of a computer system
🗌 Input devices are used to enter data from the outside world into primary storage
🗌 Output devices supply results of processing from primary storage to users

## Slide 4: Role of I/O Devices

## Slide 5: Commonly Used Input Devices
🗌 Keyboard devices
🗌 Point-and-draw devices
🗌 Data scanning devices
🗌 Digitizer
🗌 Electronic cards based devices
🗌 Speech recognition devices
🗌 Vision based devices

## Slide 6: Keyboard Devices
🗌 Allow data entry into a computer system by pressing a set of keys (labeled buttons) neatly mounted on a keyboard connected to a computer system
🗌 101-keys QWERTY keyboard is most popular

## Slide 7: The Layout of Keys on a QWERTY Keyboard
A typical computer keyboard comprises sections with different types of keys

## Slide 8: Point-and-Draw Devices
🗌 Used to rapidly point to and select a graphic icon or menu item from multiple options displayed on the Graphical User Interface (GUI) of a screen
🗌 Used to create graphic elements on the screen such as lines, curves, and freehand shapes
🗌 Some commonly used point-and-draw devices are mouse, track ball, joy stick, light pen, and touch screen

## Slide 9: Mouse
🗌 Mouse is most popular pointing device. It is a very famous cursor- control device having a small palm size box with a round ball at its base which senses the movement of mouse and sends corresponding signals to CPU when the mouse buttons are pressed.
🗌 Generally it has two buttons called left and right button and a wheel is present between the buttons. Mouse can be used to control the position of cursor on screen, but it cannot be used to enter text into the computer.
🗌 Advantages
🗌 Easy to use
🗌 Not very expensive
🗌 Moves the cursor faster than the arrow keys of keyboard.

## Slide 10: Trackball
🗌 Track ball is an input device that is mostly used in notebook or laptop computer, instead of a mouse.
🗌 This is a ball which is half inserted and by moving fingers on ball, pointer can be moved. Since the whole device is not moved, a track ball requires less space than a mouse.
🗌 A track ball comes in various shapes like a ball, a button and a square.

## Slide 11: Joystick
🗌 Joystick is also a pointing device which is used to move cursor position on a monitor screen.
🗌 It is a stick having a spherical ball at its both lower and upper ends. The lower spherical ball moves in a socket. The joystick can be moved in all four directions.
🗌 Commonly used for video games, flight simulators, training simulators, and for controlling industrial robots

## Slide 12: Light Pen
🗌 Pen-based point-and-draw device
🗌 Used to directly point with it on the screen to select menu items or icons or directly draw graphics on the screen
🗌 Can write with it on a special pad for direct input
of written information to a system
🗌 Pressure on tip of a side button is used to cause same action as right-button-click of a mouse
🗌 It consists of a photocell and an optical system placed in a small tube.
🗌 When the tip of a light pen is moved over the monitor screen and pen button is pressed, its photocell sensing element detects the screen location and sends the corresponding signal to the CPU.

## Slide 13: Touch Screen
g
🗌 Most simple, intuitive, and easiest to
learn of all input devices
🗌 Enables users to choose from available options by simply touchin with their finger the desired icon or menu item displayed on the screen
🗌 Most preferred human-computer interface used in information kiosks (unattended interactive information systems such as automatic teller machine or ATM)

## Slide 14: Data Scanning Devices
🗌 Input devices that enable direct data entry into a computer system from source documents
🗌 Eliminate the need to key in text data into the computer
🗌 Due to reduced human effort in data entry, they improve data accuracy and also increase the timeliness of the information processed
🗌 Demand high quality of input documents
🗌 Some data scanning devices are also capable of recognizing marks or characters
🗌 Form design and ink specification usually becomes more critical
for accuracy

## Slide 15: Scanner
🗌 Scanner is an input device which works more like a photocopy machine. It translates paper documents into an electronic format for storage in a computer
🗌 It is used when some information is available on a paper and it is to be transferred to the hard disc of the computer for further manipulation.
🗌 Scanner captures images from the source which are then converted into the digital form that can be stored on the disc. These images can be edited before they are printed.

## Slide 16: Optical Character Recognition (OCR) Device
🗌 Scanner equipped with a character recognition software (called OCR software) that converts the bit map images of characters to equivalent ASCII codes
🗌 Enables word processing of input text and also requires less storage for storing the document as text rather than an image
🗌 OCR software is extremely complex because it is difficult to make a computer recognize an unlimited number of typefaces and fonts
🗌 Two standard OCR fonts are OCR-A (American standard) and OCR-B (European standard)

## Slide 17: Optical Mark Reader (OMR)
🗌 Scanner capable of recognizing a pre-specified type of mark by pencil or pen
🗌 Very useful for grading tests with objective type questions, or for any input data that is of a choice or selection nature
🗌 Technique used for recognition of marks involves focusing a light on the page being scanned and detecting the reflected light pattern from the marks

## Slide 18: Sample Use of OMR

## Slide 19: Bar-code Reader
🗌 Bar Code Reader is a device used for reading bar coded data (data in form of light and dark lines)
🗌 Scanner used for reading (decoding) bar- coded data
🗌 Bar codes represent alphanumeric data by a combination of adjacent vertical lines (bars) by varying their width and the spacing between them
🗌 Scanner uses laser-beam to stroke across pattern of bar code. Different patterns of bars reflect the beam in different ways sensed by a light-sensitive detector
🗌 Universal Product Code (UPC) is the most
widely known bar coding system

## Slide 20: An Example of UPC Bar Code

## Slide 21: QR (Quick Response) Code
A matrix barcode (or two-dimensional code), readable by QR scanners, mobile phones with a camera, and smartphones.
Has various numbers of functions: linking to websites, send SMS functions, etc.
Certain applications on a smart phone / portable gaming device can scan QR codes (i.e ZXing on Android)

## Slide 22: Magnetic-Ink Character Recognition (MICR)
🗌 MICR is used by banking industry for faster
processing of large volume of cheques
🗌 Bank’s identification code (name, branch, etc.), account number and cheque number are pre-printed (encoded) using characters from a special character set on all cheques
🗌 Special ink is used that contains magnetizable particles of iron oxide
🗌 This reading process is called Magnetic Ink Character Recognition (MICR). The main advantages of MICR is that it is fast and less error prone.

## Slide 23: MICR Character Set (E13B Font)
🗌 It consists of numerals 0 to 9 and four special characters
🗌 MICR is not adopted by other industries because it supports only 14 symbols

## Slide 24: MICR Character Example

## Slide 25: Digitizer
🗌 Input device used for converting (digitizing) pictures, maps
and drawings into digital form for storage in computers
🗌 Commonly used in the area of Computer Aided Design (CAD) by architects and engineers to design cars, buildings medical devices, robots, mechanical parts, etc.
🗌 Used in the area of Geographical Information System (GIS) for
digitizing maps available in paper form
🗌 Digitizer is also known as Tablet or Graphics Tablet because it converts graphics and pictorial data into binary inputs. A graphic tablet as digitizer is used for doing fine works of drawing and image manipulation applications.

## Slide 26: Electronic-card Reader
🗌 Electronic cards are small plastic cards having encoded data appropriate for the application for which they are used
🗌 Electronic-card reader (normally connected to a computer) is used to read data encoded on an electronic card and transfer it to the computer for further processing
🗌 Used together as a means of direct data entry into a computer system
🗌 Used by banks for use in automatic teller machines (ATMs) and by organizations for controlling access of employees to physically secured areas

## Slide 27: Speech Recognition Devices
🗌 Input device that allows a person to input data to a computer
system by speaking to it
🗌 Today’s speech recognition systems are limited to accepting few words within a relatively small domain and can be used to enter only limited kinds and quantities of data

## Slide 28: Uses of Speech Recognition Systems
🗌 For inputting data to a computer system by a person in situations where his/her hands are busy, or his/her eyes must be fixed on a measuring instrument or some other object
🗌 For data input by dictation of long text or passage for later editing and review
🗌 For authentication of a user by a computer system based
on voice input
🗌 For limited use of computers by individuals with physical disabilities

## Slide 29: Vision-Input Systems
🗌 Allow computer to accept input just by seeing an object.
🗌 Input data is normally an
object’s shape and features
in the form of an image
🗌 Mainly used today in factories for designing industrial robots that are used for quality-control and assembly processes

## Slide 30: Commonly Used Output Devices
🗌 Monitors
🗌 Printers
🗌 Plotters
🗌 Screen image projector
🗌 Voice response systems

## Slide 31: Types of Output
🗌 Soft-copy output
🗌 Not produced on a paper or some material that can be touched and carried for being shown to others
🗌 Temporary in nature and vanish after use
🗌 Examples are output displayed on a terminal screen or spoken out by a voice response system
🗌 Hard-copy output
🗌 Produced on a paper or some material that can be touched and
carried for being shown to others
🗌 Permanent in nature and can be kept in paper files or can be looked at a later time when the person is not using the computer
🗌 Examples are output produced by printers or plotters on paper

## Slide 32: Monitors
🗌 Monitors are the most popular output devices used for producing soft-copy output
🗌 Display the output on a television like screen
🗌 Monitor associated with a keyboard is called a video display terminal (VDT).
🗌 It is the most popular I/O device

## Slide 33: Types of Monitors
🗌 Cathode-ray-tube (CRT) monitors look like a television and
are normally used with non-portable computer systems
🗌 Flat-panel monitors are thinner and lighter and are commonly used with portable computer systems like notebook computers. Now they are also used with non- portable desktop computer systems because they occupy less table space.

## Slide 34: Printers
🗌 Most common output devices for producing hard-copy output
🗌 There are two types of printers:
🗌 Impact Printers
🗌 Non-Impact Printers
🗌 Some widely used printers
🗌 Dot-Matrix Printers
🗌 Inkjet Printers
🗌 Drum Printers
🗌 Chain/Band Printers
🗌 Laser Printers

## Slide 35: Impact Printers
🗌 The impact printers print the characters by striking them on the ribbon which is then pressed on the paper.
🗌 Characteristics of Impact Printers are the following:
🗌 Very low consumable costs
🗌 Very noisy
🗌 Useful for bulk printing due to low cost
🗌 There is physical contact with the paper to produce an image
🗌 These printers are of two types
🗌 Character printers : Print one character at a time.
🗌 Line printers : Print one line at a time.

## Slide 36: Non-impact Printers
🗌 Non-impact printers print the characters without using ribbon.
🗌 Characteristics of Non-impact Printers
🗌 Faster than impact printers.
🗌 They are not noisy.
🗌 High quality.
🗌 Support many fonts and different character size.
🗌 These printers are of two types
🗌 Laser Printers
🗌 Inkjet Printers

## Slide 37: Dot-Matrix Printers
🗌 In the market one of the most popular printers is Dot Matrix Printer.
🗌 These printers are popular because of their ease of printing and economical price.
🗌 Each character printed is in form of pattern of dots and head consists of a Matrix of Pins of size (5*7, 7*9, 9*7 or 9*9) which come out to form a character that is why it is called Dot Matrix Printer.
🗌 Advantages
🗌 Cheap in both initial cost and cost of operation
🗌 can be used for generating multiple copies by using carbon paper or its equivalent
🗌 Other language characters can be printed
🗌 Disadvantages
🗌 Slow, with speeds usually ranging between 30 to 600 characters per second
🗌 Poor Qualit

## Slide 38: Dot-Matrix Printers

## Slide 39: Inkjet Printers
🗌 Prints characters and all kinds of images by spraying
small drops of ink on to the paper
🗌 Print head contains up to 64 tiny nozzles that can be selectively heated up in a few micro seconds by an integrated circuit register
🗌 To print a character, the printer selectively heats the appropriate set of nozzles as the print head moves horizontally
🗌 Can print many special characters, different sizes of print, and graphics such as charts and graphs

## Slide 40: Inkjet Printers
🗌 Non-impact printers. Hence, they cannot produce multiple copies of a document in a single printing
🗌 Can be both monochrome and
color
🗌 Slower than dot-matrix printers with speeds usually ranging between 40 to 300 characters per second
🗌 More expensive than a dot-matrix printer

## Slide 41: Drum Printers
🗌 Have a solid cylindrical drum with characters embossed on its surface in the form of circular bands
🗌 The surface of drum is divided into number of tracks.
🗌 Total tracks are equal to size of paper i.e. for a paper width of 132 characters, drum will have 132 tracks.
🗌 A character set is embossed on track. The different character sets available in the market are 48 character set, 64 and 96 characters set.
🗌 One rotation of drum prints one line.
🗌 Drum printers are fast in speed and can print 300 to 2000 lines per minute.
🗌 Advantages
🗌 Very high speed
🗌 Disadvantages
🗌 Very expensive
🗌 Characters fonts cannot be changed

## Slide 42: Drum Printers

## Slide 43: Chain/Band Printers
🗌 Line printers that print one line at a time
🗌 In this printer, chain of character sets are used so it is called Chain Printer.
🗌 Consist of a metallic chain/band on which all characters of the
character set supported by the printer are embossed
🗌 Also have a set of hammers mounted in front of the chain/band in such a manner that an inked ribbon and paper can be placed between the hammers and the chain/band
🗌 A standard character set may have 48, 64, or 96 characters.

## Slide 44: Chain/Band Printers
🗌 Can only print pre-defined sets of characters that are embossed on the chain/band used with the printer
🗌 Character fonts can easily be changed.
🗌 Cannot print any shape of characters, different sizes of print, and graphics such as charts and graphs
🗌 Are impact printers and can be used for generating multiple
copies by using carbon paper or its equivalent
🗌 Typical speeds are in the range of 400 to 3000 lines per minute

## Slide 45: Chain/Band Printers

## Slide 46: Laser Printers
🗌 Page printers that print one page at a time
🗌 Consist of a laser beam source, a multi-sided mirror, a photoconductive drum and toner (tiny particles of oppositely charged ink)
🗌 To print a page, the laser beam is focused on the electro statically charged drum by the spinning multi-sided mirror
🗌 Toner sticks to the drum in the places the laser beam has
charged the drum’s surface.
🗌 Toner is then permanently fused on the paper with heat and pressure to generate the printer output
🗌 Laser printers produce very high quality output having resolutions in the range of 600 to 1200 dpi

## Slide 47: Laser Printers
🗌 Can print many special characters, different sizes of print, and
graphics such as charts and graphs
🗌 Are non-impact printers
🗌 Most laser printers are monochrome, but color laser printers are
also available
🗌 Low speed laser printers can print 4 to 12 pages per minute. Very high-speed laser printers can print 500 to 1000 pages per minute
🗌 More expensive than other printers
🗌

## Slide 48: Laser Printers
🗌 Can print many special characters, different sizes of print, and graphics such as charts and graphs
🗌 Are non-impact printers
🗌 Most laser printers are monochrome, but color laser printers are also available
🗌 Low speed laser printers can print 4 to 12 pages per minute. Very high-speed laser printers can print 500 to 1000 pages per minute
🗌 More expensive than other printers

## Slide 49: Plotters
🗌 Plotters are an ideal output device for architects, engineers, city planners, and others who need to routinely generate high-precision, hard-copy graphic output of widely varying sizes
🗌 Two commonly used types of plotters are:
🗌 Drum plotter, in which the paper on which the design has to be made is placed over a drum that can rotate in both clockwise and anti-clockwise directions
🗌 Flatbed plotter, in which the paper on which the design has to
be made is spread and fixed over a rectangular flatbed table

## Slide 50: Plotters

## Slide 51: Projector
🗌 An output device that can be directly plugged to a computer system for projecting information from a computer on to a large screen
🗌 Useful for making presentations to a group of people with direct use of a computer
🗌 Full-fledged multimedia presentation with audio, video, image, and animation can be prepared and made using this facility

## Slide 52: Projector

## Slide 53: Voice Response Systems
🗌 Voice response system enables a computer to talk to a user with an audio- response device that produces audio output
🗌 Such systems are of two types:
🗌 Voice reproduction systems
Produce audio output by selecting an appropriate audio output from a set of pre-recorded audio responses
Applications include audio help for guiding how to operate a system, automatic answering machines, video games, etc.
🗌 Speech synthesizers
Converts text information into spoken sentences
Used for applications such as:
🗌 Reading out text information to blind persons
🗌 Allowing those persons who cannot speak to communicate effectively
🗌 Translating an entered text into spoken words in a selected language

## Slide 54: Key Words/Phrases

## Slide 55: Key Words/Phrases