## Slide 1
Logic Gates & Circuits
Zannatul Mawa Koli
Lecturer
Department of CSE
Daffodil International University

## Slide 2: Logic Gates
Logic gates are electronic circuits that operate on one or more input signals to produce standard output signal
Are the building blocks of all the circuits in a computer
Some of the most basic and useful logic gates are -
  AND,
  OR,
  NOT,
  NAND and
  NOR gate

## Slide 3: AND Gate
Physical realization of logical multiplication (AND) operation
Generates an output signal of 1 only if all input signals are also 1
AND Gate (Block Diagram Symbol and Truth Table)

## Slide 4: OR Gate
Physical realization of logical addition (OR) operation
Generates an output signal of 1 if at least one of the input signals is also 1
OR Gate (Block Diagram Symbol and Truth Table)

## Slide 5: NOT Gate
Physical realization of complementation operation
Generates an output signal, which is the reverse of the input signal

## Slide 6: NAND Gate
Complemented AND gate
Generates an output signal of:
① 1 if any one of the inputs is a 0
② 0 when all the inputs are 1

## Slide 7: NOR Gate
Complemented OR gate
Generates an output signal of:
① 1 only when all inputs are 0
② 0 if any one of inputs is a 1

## Slide 8: Logic Circuits
When logic gates are interconnected to form a gating / logic network, it is known as a combinational logic circuit
The Boolean algebra expression for a given logic circuit can be derived by systematically progressing from input to output on the gates
The three logic gates (AND, OR, and NOT) are logically complete because any Boolean expression can be realized as a logic circuit using only these three gates

## Slide 9: Finding Boolean Expression of a Logic Circuit (Example 1)

## Slide 10: Finding Boolean Expression of a Logic Circuit (Example 2)

## Slide 11: Constructing a Logic Circuit from a Boolean Expression (Example 1)

## Slide 12: Constructing a Logic Circuit from a Boolean Expression (Example 2)

## Slide 13: Universal NAND Gate
NAND gate is an universal gate, it is alone sufficient to implement any Boolean expression
To understand this, consider:
  Basic logic gates (AND, OR, and NOT) are logically complete
  Sufficient to show that AND, OR, and NOT gates can be implemented with NAND gates

## Slide 14: Implementation of NOT, AND and OR Gates by NAND Gates

## Slide 15: Universal NOR Gate
NOR gate is an universal gate, it is alone sufficient to
implement any Boolean expression
To understand this, consider:
  Basic logic gates (AND, OR, and NOT) are logically complete
  Sufficient to show that AND, OR, and NOT gates can be implemented with NOR gates

## Slide 16: Implementation of NOT, OR and AND Gates by NOR Gates