## Slide 1: Costing of Garment: Direct and indirect Cost
Direct Cost: A cost that can be directly attributed to the production of specific goods or services is called direct cost. Direct costs refer to materials, labor and expenses related to the production of a product.
Example:
Salary of directly engaged worker
Fabric and accessories cost

## Slide 2: Costing: Indirect Cost
Indirect Cost: Indirect costs are the costs that are not directly accountable to a cost of a product. These are those costs which are not directly related to production.
    Example:
  Utilities
  Rent
  Audit and legal expenses
  Administrative staff
  Equipment rental
  Fuel
  Maintenance
  Generator
  Security
  Telephone
  Business travel expenditure

## Slide 3: Typical Cost Breakdown of Garments
Cost Break Down for RMG with respect to FOB%
Chart: FABRIC CM ACCESSORIES
| FOB | WOVEN | KNIT | SWEATER | AVG
 | 0 | 0.5254 | 0.5876 | 0.467 | 0.52667
 | 1 | 0.1587 | 0.1153 | 0.1208 | 0.1316
 | 0 | 0.3159 | 0.2971 | 0.4122 | 0.34173

## Slide 4: Factors Affecting Costing
Yarn/ Fibre content
Yarn count and type (carded or combed)
Knitting pattern/ Fabric construction
Finishing of fabric
Type of dyes and chemicals to be used
Tolerance in shade variation
Level of Acceptable Quality Level (AQL)
Inspection authority
Lab test requirement
Design of garments
Matching instruction in case of Yarn Dyed (Y/D) and printed fabrics
Notes: 22 factors

## Slide 5: Factors Affecting Costing
Cost of making (CM)
Details of accessories and their sources
Details of printing
Details of embroidery
Details of value adding work, if any
Production lead time
Quantity of garments
Number of color and size in the order
Size and color ratio
Tolerance in measurement
Any hidden losses/costs
Notes: 22 factors

## Slide 6: Costing of a knit order
Lets, Order Quantity: 10000 pieces, Consumption per dozen: 2.18 kg
1.1 Fabric costing
100% cotton, single jersey, 190 GSM, combed yarn.
Yarn price (22’s)…………………………………………………………....$ 3.40/ kg
Landed cost………………………………………………………………...$ 0.08 /kg
Knitting charge…………………………………………………………… $ 0.25/ kg
$ 3.73/ kg
Process loss in knitting is 2%...............................................(3.73X 2%} = $ 0.08/ kg
Grey fabric cost $ 3.81/kg
Dyeing charge…………………………………………………………..…$1.50 / kg
$ 5.31/ kg
Process loss in dyeing 12%……………………………...…(5.31x12%) = $ 0.64 /kg
Finished fabric cost $5.95/ kg
Per dozen fabric cost (5.95 x 2.18) = $ 12.97
Garments quantity 10,000 pieces
Overall fabric cost= (12.97 X 10,000)/12
= $ 10,808

## Slide 7
SL | Name | Qty.(pcs) | Wastage | Total Qty. (pcs) | Unit price | Price/dz | Total price
A | Main label | 10,000 | 3% | 10,300 | $0.017 | $0.204 | $175.1
B | Size label | 10,000 | 3% | 10,300 | $0.01 | $0.12 | $103
C | Care label | 10,000 | 3% | 10,300 | $0.017 | $0.204 | $175.1
D | Sewing thread | 80*1.12*10,000/4000 | 12% | 224 cones | $ 0.95 | $0.255 | $212.8
E | Back board | 10,000 | 2% | 10,200 | $0.05 | $0.6 | $510
F | Poly bag | 10,000 | 2% | 10,200 | $0.042 | $0.504 | $428.5
G | Carton | 10,000/20 | no | 500 carton | $1.50 | $0.9 | $750
H | Hang tag/ Price tag | 10,000 | 2% | 10,200 | $0.02 | $0.24 | $204
I | Tag pin | 10,000/4500 | no | 3 box | $1.13 | $0.032 | $3.39
J | Gum tape | 500/8 | no | 63 | $0.35 | $0.26 | $22.05
K | Snap button | 10,000 * 7 | 2% | 71,400 set | $ 0.04 | $3.36 | $ 2856
Total accessories cost |  |  |  |  |  | $6.7 | $ 5441
1.2 Accessories costing

## Slide 8: Costing: CM
  1.3 Cost of making/manufacturing (CM)
  Let, Total Monthly factory cost: BDT 50,00000.00
  Let, Total numbers of machine:100
  Per Machine cost/month : 50,00,000/100= BDT 50,000
  Per Machine cost/hour: 50,000/208= BDT 240
  Let, Numbers of machine per line=15
  Let, Production of that line per hour=120
  Total machine cost of that line: 15*240= BDT 3600
  So, Per piece production cost: 3600/120= 30
  Per dozen production cost= 30*12 = 360
  So, CM in DU $ = $ 360/80 = $ 4.50
  So CM for 10000 pieces = (10000*4.5)/12= $ 3,750

## Slide 9: Costing: Other
  1.4 Printing cost
All over print cost $1.50/kg
Total print cost = 1.50*2.18*10,000/12
= $ 2,725
  1.5 Sample making cost= $ 100
1.6 Testing cost= $ 100
  1.7 Courier cost= $ 300

## Slide 10: Costing: Other
  Total cost (1.1-1.7)
  = $ (10,808+5441+3,750+2,725+100+100+300)
  = $ 23,224
  1.8 Documentation cost (1%) = $ 233
Total cost (1.1-1.8) = $ 23,457
  1.9 Buying house commission (5%) = $ 1173
Total cost (1.1-1.9) = $ 24,630
1.10 Transportation to Ctg (FOB-Ctg) port = $ 400
Total Cost – FOB Ctg (1.1-1.10) = $ 25,030

## Slide 11: Costing of a knit order
Total Direct Cost: $ 25,030
Indirect Cost (15%) : $ 25,030 x 0.15% = $ 3755
Cost of production (COP)= $ 25,030+$ 3755 = $ 28,785
Profit : 10% | Quoted Price/dozen
$ 28785 | $ 3.17*12
(10%) + $ 2879 | $ 38.04
$ 31,664 | 
Unit price | 
$ 31,664 /10000 | 
$3.17 | 

## Slide 12: Home Work: CM Calculation
Running cost of a garment factory is BDT 55,00,000 per month and the number of machine of that factory is 85. To produce of that garment a line is allocated consisting 5 machine that produces 110 pieces garments per hour. Find out the cost of making (CM) of per dozen garment of that order in US $ considering conversion rate $ 1=BDT 84.

## Slide 13: Solution
  Total monthly factory cost: BDT 55,00,000
  Total numbers of machine: 85
  Per machine cost/month : 55,00,000/85= BDT 64,706
  Per Machine cost/hour: 64706/208= BDT 311
  Numbers of machine per line=15
  Production of that line per hour=110
  Total machine cost of that line: 15*311= BDT 4665
  So, Per piece production cost: 4665/110= BDT 42.41
  Per dozen production cost= 42.41*12 = 509
  So, CM in DU $ = $ 509/84 = $ 6.06

## Slide 14: Costing: woven garment
Fabric Cost / dz = $ 2.00x22 = $ 44
Accessories /dz = $ 8.00
Wash/dz = $ 5.00
CM/dz = $ 20.00
Bank Charge (BC) = $ 1.00
……………………………………………………
Quoted price /dz = $ 78
Quoted price/pc = $ 6.5