## Slide 1: Depreciation - Definition
Any equipment which is purchased today will not work for ever. This may be due to wear and tear of the equipment or obsolescence of technology. Hence, it is to be replaced at the proper time for continuance of any business.
The replacement of the equipment at the end of its life involves money. This must be internally generated from the earnings of the equipment.
The recovery of money from the earnings of an equipment for its replacement purpose is called depreciation fund since we make an assumption that the value of the equipment decreases with the passage of time. Thus, the word “depreciation” means decrease in value of any physical asset with the passage of time.

## Slide 2: METHODS OF CALCULATING DEPRECIATION
There are several methods of accounting depreciation fund. These are as follows:
    1. Straight line method of depreciation
    2. Declining balance method of depreciation
    3. Sum of the years—digits method of depreciation
    4. Sinking-fund method of depreciation
    5. Service output method of depreciation

## Slide 3: Straight line method of depreciation
In this method of depreciation, a fixed sum is charged as the depreciation amount throughout the lifetime of an asset such that the accumulated sum at the end of the life of the asset is exactly equal to the purchase value of the asset.
Here, we make an important assumption that inflation is absent.

## Slide 4: Straight line method of depreciation

## Slide 5: Calculation of Depreciation by Straight line method
Let
P = first cost of the asset,
F = salvage value of the asset,
n = life of the asset,
Bt = book value of the asset at the end of the period t,
Dt = depreciation amount for the period t.
The formulae for depreciation and book value are as follows:
Dt = (P – F)/n
Bt = Bt–1 – Dt = P – t × [(P – F)/n]

## Slide 6: Problem
A company has purchased an equipment whose first cost is BDT. 1,00,000 with an estimated life of eight years. The estimated salvage value of the equipment at the end of its lifetime is BDT. 20,000. Determine the depreciation charge and book value at the end of various years using the straight line method of depreciation.
Solution:
P = BDT. 1,00,000
F = BDT. 20,000
n = 8 years
Dt = (P – F)/n
= (1,00,000 – 20,000)/8
= BDT. 10,000

## Slide 7: Continued…
In this method of depreciation, the value of Dt is the same for all the years. The calculations pertaining to Bt for different values of t are summarized in Table.
Dt and Bt Values under Straight line Method of Depreciation
End of year | Depreciation | Book value
(t) | (Dt) | (Bt = Bt–1 – Dt)
0 |  | 1,00,000
1 | 10,000 | 90,000
2 | 10,000 | 80,000
3 | 10,000 | 70,000
4 | 10,000 | 60,000
5 | 10,000 | 50,000
6 | 10,000 | 40,000
7 | 10,000 | 30,000
8 | 10,000 | 20,000

## Slide 8: H.W
A 24 Gauge S/J Knitting was purchased by ABC knit composite spending BDT. 22,00000. Assumed service life of the machine is 6 years and the salvage value is 6,00000. If the working days of the machine is 335 in a year and per day production is 600 KG, Calculate the depreciation cost of per KG knit fabric in Straight line depreciation method.

## Slide 9: Solution
We know,
P = first cost of the asset,
F = salvage value of the asset,
n = life of the asset,
Dt = depreciation amount for the period t.
The formulae for depreciation and book value are as follows:
Dt = (P – F)/n
= (2200000-600000)/ 6 = 1600000/6 = 266667 BDT per year
So Per KG depreciation Cost = 266667/335*600 = BDT 1.326
Answer: BDT 1.326 per KG.

## Slide 10: Declining balance method of depreciation
In this method of depreciation, a constant percentage of the book value of the previous period of the asset will be charged as the depreciation amount for the current period.
This approach is a more realistic approach, since the depreciation charge decreases with the life of the asset which matches with the earning potential of the asset. The book value at the end of the life of the asset may not be exactly equal to the salvage value of the asset. This is a major limitation of this approach.

## Slide 11: Declining balance method of depreciation
Dt and Bt according to Declining Balance Method of Depreciation
End of Year (n) | Depreciation (Dt) – 20% | Book Value (Bt)
0 |  | 1,00,000.00
1 | 20,000.00 | 80,000.00
2 | 16,000.00 | 64,000.00
3 | 12,800.00 | 51,200.00
4 | 10,240.00 | 40,960.00
5 | 8,192.00 | 32,768.00
6 | 6,553.60 | 26,214.40
7 | 5,242.88 | 20,971.52
8 | 4,194.30 | 16,777.22

## Slide 12: Sum-of-the-years—digits method of depreciation
In this method of depreciation also, it is assumed that the book value of the asset decreases at a decreasing rate. If the asset has a life of eight years, first the sum of the years is computed as
Sum of the years = 1 + 2 + 3 + 4 + 5 + 6 + 7 + 8 = 36
The rate of depreciation charge for the first year is assumed as the highest and then it decreases. The rates of depreciation for the years 1–8, respectively are as follows: 8/36, 7/36, 6/36, 5/36, 4/36, 3/36, 2/36, and 1/36.

## Slide 13: Sum-of-the-years—digits method of depreciation
Dt and Bt under Sum-of-the-years-digits Method of Depreciation
End of Year (n) | Depreciation (Dt) | Book Value (Bt)
0 |  | 1,00,000.00
1 | 22,222.22 | 77,777.77
2 | 15123.45 | 62654.32
3 | 10442.38 | 52211.94
4 | 7251.65 | 44960.29
5 | 4995.58 | 39964.71
6 | 2914.09 | 34969.13
7 | 1942.73 | 33026.4
8 | 863.43 | 31083.67

## Slide 14: Sinking-fund method of depreciation
In this method of depreciation, the book value decreases at increasing rates with respect to the life of the asset.
End of Year | Fixed Depreciation | Net Depreciation | Book Value
0 | 6,504 | – | 1,00,000.00
1 | 6,504 | 6,504.00 | 93,496.00
2 | 6,504 | 7,284.48 | 86,211.52
3 | 6,504 | 8,158.62 | 78,052.90
4 | 6,504 | 9,137.65 | 68,915.25
5 | 6,504 | 10,234.17 | 58,681.08
6 | 6,504 | 11,462.27 | 47,218.81
7 | 6,504 | 12,837.74 | 34,381.07
8 | 6,504 | 14,378.27 | 20,002.80

## Slide 15: Service output method of depreciation
In some situations, it may not be realistic to compute depreciation based on time period. In such cases, the depreciation is computed based on service rendered by an asset. Let
P = first cost of the asset
F = salvage value of the asset
X = maximum capacity of service of the asset during its lifetime
x = quantity of service rendered in a period.

## Slide 16: Continued…
Then, the depreciation is defined per unit of service rendered: Depreciation/unit of service = (P – F)/X
P-F
Depreciation for x units of service in a period =------------------( x)
                X