## Slide 1: Cleaning efficiency of blow room
Cleaning efficiency of the machine is the ratio of the trash removed by the machine to that of total trash fed to the machine, expressed as percentage.
Cleaning Efficiency % = X100
= X100

## Slide 2: Cleaning efficiency
                Wastage /impurities
Blow room
Carding
Carded slivers
Raw cotton
Wastage Removed by the Blow room
Wastage Removed by the Carding machine
Lap/ Chute mat
Wastage/ impurities

## Slide 3: Calculations
Problem: 1
A cotton of 3% trash is feed to a blow room having 50% cleaning efficiency. If the card sliver contains 0.4% trash. What would be the cleaning efficiency of the card?
Problem 2. A cotton of 6% trash is feed to a blow room. If the card sliver contains 0.4% trash & cleaning efficiency of carding 75%, what would be the cleaning efficiency of the blow room?

## Slide 4: Solution 1
Problem: 1
A cotton of 3% trash is feed to a blow room having 50% cleaning efficiency. If the
card sliver contains 0.4% trash. What would be the cleaning efficiency of the card?
Solution:
We know,
Cleaning Efficiency % = X100
= X100

## Slide 5: Solution 1
Here, Cleaning Efficiency of blow room %=
X100
So, 50 = x100
or, 150 = 100(3-trash in lap)
or, 150 +100 X trash in lap = 300
or, trash in lap = 150/100
Therefore, trash in lap =1.5%

## Slide 6: Solution 1
Cleaning Efficiency of carding %=
X100
= X 100
= X 100
= 73.33
Therefore, cleaning efficiency of carding machine is 73.33%.

## Slide 7: Rieter Blow room line
Unifloc B 12
Uniclean B11
Unimix B60
Uniflex B70
FFD (Vission Shield, Jossi)
Condenser A21

## Slide 8: Trutzschler Blow Room line
Blendomat BO
Precleaner CLP
Multimixer MPM
Fine Cleaner CLC
FFD (SP EP, Securo, Prop, Securomat)
Dustex

## Slide 9: Automatic bale opener
Features of automatic bale opener:
Gentle Uniform Opening
Production up to 1500 Kg/hr
Easy operation
Minimal maintenance
Universally applicable

## Slide 10: Automatic bale opener:
Up to 3 bale groups at the same time
Up to 180 bales in the lay down
Feeding in up to 3 lines
Processing by lot or continuously bale supply
Process visualization

## Slide 11: Automatic bale opener:

## Slide 12: Automatic bale opener

## Slide 13: Working Principle of Blendomat/Unifloc( Automatic bale opener)

## Slide 14: Parts name of the machine
The machine parts for automatic bale opener:
A) Tower
B) Suction hood
C) Track or rail for machine
D) Take off roller or plucker
E) Control panel
F) Sensors

## Slide 16: Precleaner/ Uniclean (coarse cleaner)

## Slide 17: Parts name of the machine
A) Inlet
B) Cleaning roller or Spiked roller (Beaters)
C) Grids
D) Bucket wheel trap for waste extraction
E) Outlet

## Slide 18: Multimixer/Multiple Mixer/UNimix

## Slide 19: Parts name of the machine
Inlet
Feed duct
Mixing Chambers
Closing Flap
Sensors
Perforated wall
Opening roller
Blending roller
Blending Duct
Outlet

## Slide 20: Finecleaner / Uniflex (fine particle cleaner)

## Slide 21: Parts name of the machine
A) Coarse saw toothed roller
B) Medium saw toothed roller
C) Fine saw toothed roller
D) Suction hood
E) Deflector blade
F) Mote knife

## Slide 22: Dedusting Machine

## Slide 23: Foreign Metal detector

## Slide 24: Foreign Metal detector