## Slide 1: Necessities of Auto stop motion
Stop motion is a device which provided to ensure in the machine are stopped immediately if: –
1. The sliver run out from the creeled can.
2. Sliver brakes in the creel.
3. Roller lapping on drafting roller.
4. If sliver is chocked in the sliver collecting plate and funnel.
5. If sliver is chocked in between trumpet and calendar roller.
6. If delivery can is filled with sliver.

## Slide 2
If stop motion system is absent then the following defects may arise:-
1. Considerable damage may cause to machine.
2. The output sliver may be thick or thin.
3. Lapping up of drafting or calendar roller.
4. Irregular drafting.
5. Excess of full can.
6. Too much waste produce.
7. The yarn strength or roving strength may vary from place to place.
8. Any operator must have to attend the machine full time to stop it at any fault.

## Slide 3: Differences between carded sliver and drawn sliver
Carded sliver | Drawn sliver
Carded slivers contains crimped and hook fiber. | Drawn slivers contain less number of crimped and hook fibres as they are being straighten by drawing process.
The weight per unit length of carded slivers is irregular. | The weight per unit length of drawn slivers is more uniform.
Fibers are not parallel to each other | Fibers are more parallel
Contains more dust in fibre | Contain less or no dust in fibre
The carded slivers are coarser than drawn sliver | The drawn slivers are finer than carded sliver
Many projectile fibres come out from the sliver axis. | Less projectile fibers come out from the sliver axis.

## Slide 4: Effect of drafting and doubling on sliver quality:
Effects of doubling:
Weight per unit length of slivers increase due to doubling process.
With the increase of doubling the variations of weight per unit length of sliver reduces.
Effects of drafting:
Weight per unit length decreases due to drafting
With the increase of drafting sliver irregularity also increases.
The dirt and dust are eliminated due to drafting process as the process involves fibre to fibre and fibre to metal friction.

## Slide 5: Features of modern Draw frame
Improved drafting system.
Can linking system.
Rectangular can.
Fault locating induction lamp.
Monitoring system.
Automatic can charger.
Suction system for drafting arrangement.
High speed of production.
High draft.
Better control of short fiber.
Auto leveling.
Auto stop motion system.
Auto drafting and display unit.
Electronic control and display unit.