## Slide 1: Introduction to TCP/IP
Professor Dr. A.K.M Fazlul Haque
Department of Electronics and Telecommunication Engineering (ETE)
Daffodil International University

## Slide 2: TCP/IP model
TCP/IP reference model
• Created by the Department of Defence (DoD)
• Wanted reliable data transmission to any destination on a network
• Multiple cable runs, fiber, satellite links, etc.
• Current version standardized in Sept 1981.

## Slide 3: TCP/IP model (Cont.)
• Addressing:
• IPv4
• 32 bits, written in dotted decimal
• 4 octets, separated by dots
• i.e. 131.107.3.10
•IPv6 (or IPng)
• 128 bits, written in hexadecimal
• 16 bit fields separated by colons
• i.e. 3ffe : 1900 : 3 : 230 : f804 : 7ebf : 12c2

## Slide 4: Application layer
Application Layer:
• high-level protocols
• data representation,
encoding and dialog
control.

## Slide 5: Application Layer Protocols
FTP
– Reliable, connection-oriented service (uses TCP)
– Transfer files between systems
– Bi-directional binary and ASCII file transfers
TFTP
– Connectionless service (uses UDP)
– Used on router to transfer configuration files
– Faster than FTP

## Slide 6: Application Layer Protocols (Cont.)
NFS
– Distributed file system developed by Sun
– Allows file access to remote storage across a network
SNMP
– Network management protocol
– Monitors and control network devices
DNS
– Translates names into IP addresses

## Slide 7: Transport layer
Provides transport services from the source to the destination.
Logical connection between endpoints.
UDP:
– Connectionless
– Unacknowledged
TCP:
– Connection-oriented
– Flow control – sliding windows
– Reliability provided by sequence numbers and acknowledgements.

## Slide 8: Internet layer
Selects the best path through the network for the packets
  to travel
IP:
– Connectionless
– Best-effort delivery (no error checking or correction)
– Not concerned with contents, but with path determination

## Slide 9: Internet layer (Cont.)
ICMP:
– Control & messaging
ARP:
– Determines the MAC address for a
known IP address
RARP:
– Determines IP address with the MAC address is known.

## Slide 10: Network access layer
Defines the procedures for
interfacing with the network
hardware and accessing the
transmission medium.
Drivers for software applications,
modem cards and other devices
operate at the network access layer.

## Slide 11: TCP/IP Vs OSI
Similarities of the OSI
and TCP/IP models:
•Both have layers
•Both have comparable
transport and network layers.
•Packet-switched, not circuit-
switched technology is assumed
•Networking professionals need to
know both models.

## Slide 12: Differences of the OSI and TCP/IP models
TCP/IP combines the presentation and session layer into
its application layer
TCP/IP combines the OSI data link and physical layers
into one layer
TCP/IP appears simpler because it has fewer layers
TCP/IP transport layer using UDP does not always
guarantee reliable delivery of packets as the transport
layer in the OSI model does

## Slide 13: Internet architecture
LANs have distance restrictions.
An internet is a network of networks.
• Must be able to handle vast
distances.
• Must be flexible to include
different technology
• Cost-effective,
“anytime, anywhere”
data communication.