## Slide 1: Computer Networks
RIP
Professor Dr. A.K.M Fazlul Haque
Electronics and Telecommunication Engineering
(ETE)
Daffodil International University
GAA
Global Access Asia

## Slide 2: What is RIP?
RIP is a routing protocol for exchanging routing table information between routers.
  Routing updates must be passed between routers so that they can make the proper choice on how to route a packet.

## Slide 3: Background to RIP
RIP dates back to 1969, the early networking days and ARPNET when Xerox and Berkley’s Unix implemented it broadly similar protocols.
RIP distributed through ‘route d’ application, included in early Unix O.S.
RIP uses a single class of routing algorithm known as distance vector - based on a simple hop count algorithm (derived from Bellman’s equation).
Although superseded by more complex algorithms, its simplicity means is still found widely in smaller autonomous systems.

## Slide 4: Purpose of Routing Information Protocol
The purpose of Routing protocols is to supply information needed to do routing of datagrams from router to router.
RIP intended for use in IP based network environment.
Operating at layer 3 of OSI (Network)
RIP makes no formal distinction between networks and hosts.
Routers typically provide a gateway for datagrams to leave one network or AS and be forwarded onward to another network.
Routers therefore, have to make decisions if there is a choice of forwarding path on offer.

## Slide 5: RIP Characteristics
A classful, Distance vector routing protocol.
Uses hop count as a path selection metric.
Updates are broadcast every 30 seconds.
Multiple stability features.

## Slide 6: Versions
There are two versions of the Routing Information Protocol:
RIPv1- The original specification of RIP, defined in RFC 1058, was published in 1988 and uses classful routing.
RIPv2- RIP version 2 (RIPv2) was developed in 1993 and last standardized in 1998.

## Slide 7: Difference between RIPv1 & RIPv2
    RIPv1
      A classful distance vector routing protocol
      Does not support discontinuous subnets
      Does not support VLSM
      Does not send subnet mask in routing update
      Routing updates are broadcast
    RIPv2
      A classless distance vector routing protocol that is an enhancement of RIPv1’s features
      Next hop address is included in updates
      Routing updates are multicast
      The use of authentication is an option

## Slide 8: Similarities between RIPv1 & RIPv2
  Use of timers to prevent routing loops
  Use of split horizon or split horizon with poison reverse
  Maximum hop count of 15

## Slide 9: RIPv1 Features

## Slide 10: RIPv1 Limitations
Scenario:
  3 router set up
  Topology is discontinuous
  There exists a static summary route
  Static route information can be injected into routing table updates using redistribution.
  Routers 1 & 3 contain VLSM networks

## Slide 11: RIPv1 Limitations (cont.)
RIP Message Format:
RIP header - divided into 3 fields
  Command field
  Version field
  Must be zero
Route Entry - composed of 3 fields
  Address family identifier
  IP address
  Metric

## Slide 12: RIPv1 Limitations (cont.)
Route redistribution
  Redistribution command is way to disseminate a static route from one router to another via a routing protocol
  Example - R2(config-router)#redistribute static

## Slide 13: RIPv1 Limitations (cont.)
RIPv1 does not support VLSM
  Reason: RIPv1 does not send subnet mask in routing updates
RIPv1 does summarize routes to the Classful boundary
  Or uses the Subnet mask of the outgoing interface to determine which subnets to advertise

## Slide 14: RIPv1 Limitations (cont.)
No CIDR Support
In the diagram R2 will not include the static route in its update
  Reason: Classful routing protocols do not support CIDR routes that are summarized with a smaller mask than the classful subnet mask

## Slide 15: RIPv2 Features
RIP v2 is an improved version of RIP v1 and shares the following features:
It is a distance vector protocol that uses a hop count metric.
It uses holddown timers to prevent routing loops – default is 180 seconds.
It uses split horizon to prevent routing loops.
It uses 16 hops as a metric for infinite distance.
RIP v2 multicasts routing updates using the Class D address 224.0.0.9, which provides for better efficiency.

## Slide 16: RIP Message Format
RIP header - divided into 3 fields
  Command field
  Version field
  Must be zero
Route Entry - composed of 3 fields
  Address family identifier
  IP address
  Metric

## Slide 17: RIP Operation
  RIP uses 2 message types:
    Request message
      This is sent out on startup by each RIP enabled interface
      Requests all RIP enabled neighbors to send routing table
    Response message
      Message sent to requesting router containing routing table

## Slide 18: RIP Operation (Cont.)
IP addresses initially divided into classes
  Class A
  Class B
  Class C
RIP is a classful routing protocol
  Does not send subnet masks in routing updates

## Slide 19: Comparing RIPv1 & RIPv2 Message Formats
  RIPv2 Message format is similar to RIPv1 but has 2 extensions
    1st extension is the subnet mask field
    2nd extension is the addition of next hop address

## Slide 20: Administrative Distance of RIPv1
  RIP’s default administrative distance is 120

## Slide 21: RIPv2 & CIDR
CIDR uses Supernetting
  Supernetting is a bunch of contiguous classful networks that is addressed as a single network

## Slide 22: Verifying RIPv2
The show ip protocols and show ip route commands display information about routing protocols and the routing table. This section describes how to use show commands to verify the RIP configuration.

## Slide 23: Troubleshooting RIPv2
Networks using a VLSM IP addressing scheme
  Use classless routing protocols (i.e. RIPv2) to disseminate network addresses and their subnet masks

## Slide 24: Troubleshooting RIPv2 (Cont.)
This section explains the use of the debug ip rip command.
Use the debug ip rip command to display RIP routing updates as they are sent and received. The no debug all or undebug all commands will turn off all debugging.

## Slide 25
END