## Slide 1: Computer Networks
OSPF
Professor Dr. A.K.M Fazlul Haque
Department of Electronics and Telecommunication Engineering (ETE)
Daffodil International University
GAA
Global Access Asia

## Slide 2: What Is OSPF
Open Shortest Path First (OSPF) is a routing protocol for Internet Protocol (IP) networks. It uses a link state routing algorithm and falls into the group of interior routing protocols, operating within a single autonomous system (AS).

## Slide 3: Features of OSPF
Use flexible metrics instead of hop count.
Support variable-length subnetting.
Allow load balancing among equal-cost paths.
Support type of services (ToS).
Authenticate route exchanges.
Quick convergence.
Support multicast.

## Slide 4: OSPF Areas

## Slide 5: OSPF Area Types
Restrict the amount of external routing information within an area. This is used when resources especially router memory is very limited.
Two types of restricted areas:
    Stub Areas
    NSSAs or Not-So-Stubby-Areas

## Slide 6: OSPF Message Encapsulation

## Slide 7: OSPF Packet Types

## Slide 8: Hello Protocol
OSPF Hello Packet use Hello Protocol.
  Purpose of Hello Packet:
      Discover OSPF neighbors & establish adjacencies.
      Advertise guidelines on which routers must agree to become neighbors.
      Used by multi-access networks to elect a designated router and a backup designated router.

## Slide 9: Hello Packets

## Slide 10
OSPF Link-state Updates
  Purpose of a Link State Update (LSU):
      Used to deliver link state advertisements.
  Purpose of a Link State Advertisement (LSA):
      Contains information about neighbors & path costs.

## Slide 11: OSPF Algorithm
OSPF routers build & maintain link-state database containing LSA received from other routers.
  Information found in database is utilized upon execution of Dijkstra SPF algorithm.
  SPF algorithm used to create SPF tree.
  SPF tree used to populate routing table.

## Slide 12: Administrative Distance
  Default Administrative Distance for OSPF is 110.

## Slide 13: OSPF Authentication
  Purpose is to encrypt & authenticate routing information
  This is an interface specific configuration.
  Routers will only accept routing information from other routers that have been configured with the same password or authentication information.

## Slide 14: OSPF Metric
OSPF uses cost as the metric for determining the best route.
  The best route will have the lowest cost.
  Cost is based on bandwidth of an interface.
    Cost is calculated using the formula
    10^8 / bandwidth.
  Reference bandwidth is 100Mbps.
    Can be modified using Auto-cost reference-bandwidth command.

## Slide 15: COST of an OSPF route
  Cost is the accumulated value from one router to the next.

## Slide 16: Basic OSPF Configuration
Modifying the Cost of a link:
Both sides of a serial link should be configured with the same bandwidth.
  Commands used to modify bandwidth value:
    Bandwidth command
      Example:
      Router(config-if)#bandwidth 64
    Ip ospf cost command – allows you to directly specify interface cost
      Example: R1(config)#interface serial 0/0/0
      R1(config-if)#ip ospf cost 1562

## Slide 17: Basic OSPF Configuration (Cont.)
Difference between bandwidth command & the ip ospf cost command:
  Ip ospf cost command Sets cost to a specific value.
    Link cost is calculated by Bandwidth command.

## Slide 18
Neighbor in Broadcast Network

## Slide 19
OSPF Router Types

## Slide 20: OSPF and Multi-access Networks
Challenges in Multi-access Networks.
OSPF defines five network types:
  Point-to-point
  Broadcast Multi-access
  Non broadcast Multi-access (NBMA)
  Point-to-multipoint
  Virtual links

## Slide 21: OSPF and Multi-access Networks (Cont.)
Two challenges presented by multi-access networks:
  Multiple adjacencies.
  Extensive LSA flooding.

## Slide 22: OSPF and Multi-access Networks (Cont.)
Solution to LSA flooding issue is the use of:
  Designated router (DR)
  Backup designated router (BDR)
DR & BDR selection
  Routers are elected to send & receive LSA
Sending & Receiving LSA
  DR others send LSAs via multicast 224.0.0.6 to DR & BDR
  DR forward LSA via multicast address 224.0.0.5 to all other routers

## Slide 23: OSPF and Multi-access Networks (Cont.)
DR/BDR elections will take place on multi-access networks as shown below:

## Slide 24: OSPF and Multi-access Networks (Cont.)
Criteria for getting elected DR/BDR:
  DR: Router with the highest OSPF interface priority.
  BDR: Router with the second highest OSPF interface priority.
  If OSPF interface priorities are equal, the highest router ID is used to break the tie.

## Slide 25
END