## Slide 1: Computer Networks
IPV6 Introduction
Professor Dr. A.K.M Fazlul Haque
Electronics and Telecommunication Engineering
(ETE)
Daffodil International University
GAA
Global Access Asia

## Slide 2
Internet
Protocol
Number / Address
Number / Address
5 RIRs
ISPs
End Users
IP Addresses connect the Internet
Internet Addressing
GAA
Global Access Asia
Notes: IP essentially gives any devices a number and address to communicate with other devices on the Internet
Basically, IP addresses are held by the IANA → large blocks of address are located to 5 RIRs → (NIR, APNIC region) → smaller blocks to LIR/ISPs → End Users

## Slide 3: Internet Protocol version 6 (IPv6)
IPv6 is the most recent version of the Internet Protocol (IP), the communications protocol that provides an identification and location system for computers on networks and routes traffic across the Internet.
GAA
Global Access Asia

## Slide 4: Why IPv6?
Deficiency of IPv4
Address space exhaustion
New types of service  Integration
Multicast
Quality of Service
Security
Mobility (MIPv6)
Header and format limitations
GAA
Global Access Asia

## Slide 5: IPv6 Addressing
GAA
Global Access Asia

## Slide 6: IPv6 Addressing Examples
GAA
Global Access Asia

## Slide 7: Binary Conversion
GAA
Global Access Asia

## Slide 8
IPv6 Addressing Structure
Byte – 8 bits.
Nibble – 4 bits.
Hextet – 16 bits (4 nibbles).
GAA
Global Access Asia

## Slide 9: IPv6 Addressing Structure (Cont.)
The Site Prefix or Global Routing Prefix is the first 3 hextets or 48-bits of the address. It is assigned by the service provider.
The Site Topology or Subnet ID Is the 4th hextet of the address.
The Interface ID is the last 4 hextets or 64-bits of the address. It can be manually or dynamically as.signed using the EUI-64 command. (Extended Unique Identifier).
GAA
Global Access Asia

## Slide 10: IPv6 Addressing Structure (Cont.)
First 3 bits are fixed at 001 or 200::/12 (IANA Global Routing Number)
Bits 16-24 identifies the Regional Registry:
  - AfriNIC, APNIC, LACNIC, RIPE NCC and ARIN
    2001:0000::/23 – IANA
    2001:0200::/23 – APNIC (Asia/Pacific Region)
    2001:0400::/23 – ARIN (North America Region)
    2001:0600::/23 – RIPE (Europe, Middle East and Central Asia)
GAA
Global Access Asia

## Slide 11: IPv6 Addressing Structure (Cont.)
Remaining 8-bits up to /32 identifies the ISP.
The 3rd hextet represents the Site/Customer Identifier.
The 4th hextet represent the Site Topology/Subnet ID.
  Allows 65,536 subnets with 18,446,744,073,709,551,616 (18 quintillion) for each subnet.
  Not part of the host address field.
GAA
Global Access Asia

## Slide 12: IPv6 Addressing Scheme and Subnets
The Interface ID are the remaining 64-bits of the address.
Can be manually configured or dynamically by using the EUI-64 (Extended Unique Identifier).
The EUI-64 command uses the device 48-bits MAC Address and convert it into 64-bits by adding FF:FE in the middle of the address.
The first (network) and last (broadcast) address may be assigned to an interface. An interface may contain more than one IPv6 address.
There are no broadcast addresses, multicast is used instead.
GAA
Global Access Asia

## Slide 13: IPv6 Addressing Scheme and Subnets (Cont.)
IPv6 uses the same method as IPv4 to subnet their addresses.
/127 gives you 2 addresses.
/124 gives you 16 addresses
/120 gives you 256 addresses
The first address in a network consists of all 0's and the last address consists of all F's.
It’s recommended for simplicity and design purposes to use /64 everywhere. Using anything less than /64 could potentially break IPv6 features and cause increased design complexity.
GAA
Global Access Asia

## Slide 14: Leading Zeroes and Double Colons (::)
Leading 0s (zeroes) in any 16-bit section can be omitted.
Address before omission:
2001:0DB8:0001:5270:0127:00AB:CAFE:0E1F /64
Address after omission:
2001:DB8:1:5270:127:AB:CAFE:E1F /64
This rule applies only to leading 0s; if trailing 0s are omitted, the address would be vague.
GAA
Global Access Asia

## Slide 15: Leading Zeroes and Double Colons (::)
A Double Colons or Compressing Zeroes can be used to shorten an IPv6 address when one or more hextets consist of all 0s.
Double Colons can only be used to compress a single contiguous 16-bits blocks. You cannot use double colons to include part of a block.
Double Colons can only be used once in an address, if it's used more than once the address could be ambiguous
GAA
Global Access Asia

## Slide 16: IPv6 Address
GAA
Global Access Asia

## Slide 17: Subnetting in IPv6
GAA
Global Access Asia

## Slide 18: IPv6 Addressing Types
Address Types | IPv6 | IPv4
Unspecified | ::/128 | 0.0.0.0
Loopback | ::1 | 127.0.0.1
Global Unicast | 2000::/3 | No equivalent single block
Unique Local Addresses (Private IP Address) | fc00::/7 | 10.0.0.0/8 172.16.0.0/12 192.168.0.0/16
Link-Local Addresses | fe80::200:5aee:feaa:20a2 | 169.254.0.0/16
Multicast | ff00::/8 | 224.0.0.0/4
6to4 | 2002::/16 | There is no equivalent
IPv4-Mapped | ::ffff:192.0.2.47 | N/A
Documentation | 2001:db8::/32 | 192.0.2.0/24 198.51.100.0/24 203.0.113.0/24
GAA
Global Access Asia

## Slide 19: IPv6 Addressing Types (Cont.)
Unicast Address:
  Uniquely identifies a single interface on an IPv6 device.
  A packet sent to a unicast address destination travels from one host to the destination host.
  An interface may have more than one IPv6 address or an IPv6 and an IPv4 addresses which is referred as "Double Stack".
  When mistakes are made on Entering an address to the IPv6 interface, the user must issue the no ipv6 address command before entering the correct one or the address will remain on the interface.
GAA
Global Access Asia

## Slide 20: IPv6 Addressing Types (Cont.)
Multicast Address:
  All Multicast address are identified by their reserved address range FF00::0/8
  A packet sent to a multicast address is delivered to all devices that are identified by that address.
  A Multicast address identifies a group of interfaces.
Protocol IPv4 Multicast IPv6 Multicast
OSPF (Router) 224.0.0.5 FF02::5
OSPF (DR/BDR) 224.0.0.6 FF02::6
RIPv2 224.0.0.9 FF02::9
EIGRP 224.0.0.10 FF02::A
GAA
Global Access Asia

## Slide 21: IPv6 Addressing Types (Cont.)
Anycast Address:
  A unicast address can be assigned to several interfaces/devices.
  A packet sent to an Anycast address goes only to the nearest member of the group, according to the routing protocols measures of distance.
  Anycast is described as a cross between a Unicast and Multicast.
  The difference between an Anycast and Multicast is that in Anycast packet is only delivered to a single device, while Multicast send it to multiple devices.
GAA
Global Access Asia

## Slide 22: IPv6 Addressing Types (Cont.)
Link-Local Address:
  Link-Local address are designed for use on a single local link.
  Link-Local address are automatically configured on all interfaces.
  The prefix used for a Link-Local address is FE80::X/10.
  Routers do not forward packet with a destination and source address containing a link-local address.
Loopback Address:
  Similar function to IPv4 127.0.0.1 address
  The Loopback address is 0:0:0:0:0:0:0:1 or may be simplify by using double colons as ::1.
  It is used by a device to send a packet to itself
Representation IPv6 Loopback Address
Preferred 0000:0000:0000:0000:0000:0000:0000:0001
No Leading 0’s 0:0:0:0:0:0:0:1
Compresses ::1
GAA
Global Access Asia

## Slide 23: Acquiring Address
GAA
Global Access Asia

## Slide 24: Interface Identifier Configuration
GAA
Global Access Asia

## Slide 25: Modified EUI-64 (M-EUI-64)
Invert 7th bit “0” to “1”
64 bit
GAA
Global Access Asia

## Slide 26: IPv6 Configuration Verify
GAA
Global Access Asia

## Slide 27: IPv6 Configuration Verify(Cont.)
GAA
Global Access Asia

## Slide 28: IPv6 – ISP addressing
Every ISP receives a /32 (or more)
  Providing 65,536 site addresses (/48)
/32
/32
/32
GAA
Global Access Asia

## Slide 29: IPv6 – Site addressing
Every “site” receives a /48
  Providing 65,536 /64 (LAN) addresses
/48
GAA
Global Access Asia

## Slide 30: IPv6 – LAN addressing
Every LAN segment receives a /64
  Providing 264 interface addresses per LAN
/64
GAA
Global Access Asia

## Slide 31: IPv6 – Device addressing
Every device interface receives a /128
  May be EUI-64 (derived from interface MAC address), random number , auto-configuration, or manual configuration.
/128
/128
/128
/128
GAA
Global Access Asia

## Slide 32
IPv6 Address Space
GAA
Global Access Asia

## Slide 33
IPv6 Address Space(Cont.)
GAA
Global Access Asia

## Slide 34: Header Comparison
GAA
Global Access Asia

## Slide 35: IPv6 Transition
GAA
Global Access Asia

## Slide 36
A Dual Stack Configuration
GAA
Global Access Asia

## Slide 37
Tunnel Encapsulation and De-capsulation
GAA
Global Access Asia

## Slide 38: Routing in IPv6
As in IPv4, IPv6 has 2 families of routing protocols: IGP and EGP, and still uses the longest-prefix match routing algorithm
IGP
  RIP (RFC 2080)
  Cisco EIGRP for IPv6
  OSPFv3 (RFC 2740)
  Integrated IS-ISv6 (draft-ietf-isis-ipv6-02)
EGP : MP-BGP4 (RFC 2858 and RFC 2545)
Cisco IOS supports all of them.
GAA
Global Access Asia

## Slide 39: IPv6
128-bits address containing global routing prefix, subnet ID and interface ID.
Uses a hexadecimal format ranging from 0-9, A-F.
Maximum Transmission Unit up to 1280 bytes.
Network address and broadcasts address can be assigned to an interface or end device.
Native IPsec encryption.
32-bits addressing scheme containing a host and a network portion.
Use binary format between 0 and 1.
Maximum Transmission Unit up to 576 bytes.
Network address and broadcasts address cannot be assigned to an interface or end device.
VPN technologies must be used to encrypt IPv4 packets.
IPv4
GAA
Global Access Asia

## Slide 40
END