## Slide 1: Computer Networks
Security & Troubleshooting
Professor Dr. A.K.M Fazlul Haque
Electronics and Telecommunication Engineering (ETE)
Daffodil International University

## Slide 2
General Network Security.
Denial-of-Service Facts.
Types of Denial-of-Service Attacks.
Specific Network Attacks.
Protecting the Hardware & Software.
Layer 2 Security.
SSH, VPNs, Syslog.
SDM Security Audit.
Security Audit Wizard.
Cisco Auto-Secure.
ACL Topology and Types.
Security

## Slide 3
Security policy
  An organization’s set of rules regarding how to handle and protect sensitive data.
A security policy should include:
  Physical security
  Acceptable use of applications
  Safeguarding data
  Remote access to the network
  Data center
  Wireless security
General Network Security

## Slide 4
Commonly used against information stores like web sites.
Simple and usually quite effective.
Does not pose a direct threat to sensitive data.
The attacker tries to prevent a service from being used and making that service unavailable to legitimate users.
Attackers typically go for high visibility targets such as the web server, or for infrastructure targets like routers and network links.
Uh-Oh. Another DoS attack!
c
Denial-of-Service Facts

## Slide 5
If a mail server is capable of receiving and delivering 10 messages a second, an attacker simply sends 20 messages per second. The legitimate traffic (as well as a lot of the malicious traffic) will get dropped, or the mail server might stop responding entirely.
  This type of an attack may be used as a diversion while another attack is made to actually compromise systems.
  In addition, administrators are likely to make mistakes during an attack and possibly change a setting that creates a vulnerability that can be further exploited.
Denial-of-Service Example

## Slide 6
Physical Infrastructure Attacks
Buffer Overflow Attacks
SYN Flood Attack
Teardrop Attacks
Smurf Attack
DNS Attacks
Email Attacks
Viruses/Worms
Types of Denial-of-Service Attacks

## Slide 7
ARP Attack
Brute Force Attack
Worms
Flooding
Sniffers
Spoofing
Redirected Attacks
Tunneling Attack
Covert Channels
Specific Network Attacks

## Slide 8
The first level of security in any network is physical security.
Critical nodes of an organization should be separated from the general workforce.
The nodes should be kept in a central location where only a select group of people are allowed.
If office space is limited and nodes must be located near employees.
  The servers should at least be stored in a locked cabinet.
Protecting the Hardware

## Slide 9
The primary threats against software are malware and hackers.
Malware:
  Refers to malicious programs that have many different capabilities.
Hackers are usually driven by greed, ego, and/or vengeance.
  They look to make personal gains through system vulnerabilities.
The most important elements of a prevention plan
  Installing and maintaining virus prevention software,
  Conducting virus awareness training for network users
Types of malware:
  Virus
  Worm
  Macro Virus
  Polymorphic Virus
  Stealth Virus
Protecting The Software

## Slide 10
IPS
MARS
VPN
ACS
Iron Port
Firewall
Web Server
Email Server
DNS
Hosts
Perimeter
Internet
Layer 2 Security

## Slide 11
A firewall is a system that enforces an access control policy between network
Common properties of firewalls:
  The firewall is resistant to attacks
  The firewall is the only transit point between networks
  The firewall enforces the access control policy
Four firewall topologies:
  Packet-filtering router
  Single-homed bastion
  Dual-homed bastion
  Demilitarized zone (DMZ)
Firewalls

## Slide 12
MAC Addresses
When it comes to networking, Layer 2 is often a very weak link.
Physical Links
IP Addresses
Protocols and Ports
Application Stream
Application
Presentation
Session
Transport
Network
Data Link
Physical
Compromised
Application
Presentation
Session
Transport
Network
Data Link
Physical
Initial Compromise
OSI Model

## Slide 13
Permission:
  An official approval that allows a user to access a specific network resource.
Encryption
  Often consists of using security algorithms to scramble and descramble data.
  Types of algorithms
    Symmetric key
    Asymmetric key
Permissions, Encryption, and Authentication

## Slide 14
Secure Sockets Layer:
  A means of encrypting a session between two hosts through the use of digital certificates, which are based on asymmetric key encryption.
Authentication:
  The process by which users verify to a server that they are who they say they are.
  There are several types of authentication
    Password authentication protocol (PAP)
    Challenge handshake authentication protocol (CHAP)
Permissions, Encryption, and Authentication (Cont.)

## Slide 15
Secure Shell (SSH) protocol
  Sends all data encrypted.
The two version of SSH are SSH Version 1 and SSH Version 2.
  SSH Version 2 is the recommended version.
The preferred method is to implement SSH on all VTY lines which ensures that all remote IP sessions to the router will be protected in the SSH tunnel.
The command sequence for enabling SSH is:
  Router(config)#hostname SshRouter
  SshRouter(config)#ip domain-name sshtest.com
  SshRouter(config)#crypto key generate rsa
  The name of the keys will be: SshRouter.sshtest.com
Secure Shell (SSH) Connections

## Slide 16
Virtual Private Networks (VPNs):
  A popular technology for creating a connection between an external computer and a corporate site over the Internet.
Client-to-site VPN (also known as remote user VPN):
  A VPN that allows designated users to have access to the corporate network from remote locations.
Site-to-site VPN:
  A VPN that allows multiple corporate sites to be connected over low-cost Internet connections.
You can choose from several tunneling protocols to create secure, end-to-end tunnels. These are:
  Point-to-Point Tunneling Protocol (PPTP)
  Layer 2 Tunneling Protocol (L2TP)
  Generic Routing Encapsulation (GRE)
Virtual Private Networks (VPNs)

## Slide 17
Syslog servers: Known as log hosts, these systems accept and process log messages from syslog clients.
Syslog clients: Routers or other types of equipment that generate and forward log messages to syslog servers.
e0/0 10.2.1.1
e0/1 10.2.2.1
e0/2 10.2.3.1
User 10.2.3.3
Public Web Server 10.2.2.3
Mail Server 10.2.2.4
Administrator Server 10.2.2.5
Syslog Server 10.2.3.2
Protected LAN 10.2.3.0/24
DMZ LAN 10.2.2.0/24
Syslog Client
R3
Syslog

## Slide 18
You should disable the services unless your organization uses them.
Methods:
  Go through the CLI and enter a series of commands for each service.
  Use the Security Audit Wizard in the Cisco Security Device Manager(SDM)
The following services are unnecessary on most networks:
  Finger Service
  PAD Service
  TCP Small Servers Service
  UDP Small Servers Service
  IP Boot Server Service
  Cisco Discovery Protocol (CDP)
  Maintenance Operations Protocol (MOP)
  IP Source Route
  Directed Broadcast
  ICMP Redirects
  Proxy ARP
  IDENT
  IPv6
Disabling Unnecessary Services

## Slide 19
Perform Security Audit letting the administrator choose configuration changes to implement.
One-Step Lockdown automatically makes all recommended security-related configuration changes.
SDM Security Audit
Notes: 19

## Slide 20
Compares router configuration against recommended settings:
  Apply the firewall to the outside interfaces
  Shut down unneeded servers
  Disable unneeded services
  Disable or harden SNMP
  Shut down unused interfaces
  Check password strength
  Enforce the use of ACLs
Security Audit Wizard
Notes: 20

## Slide 21
ACL Topology and Types

## Slide 22
Standard IP ACLs
Extended IP ACLs
Extended IP ACLs using TCP established
Reflexive IP ACLs
Dynamic ACLs
Time-Based ACLs
Context-based Access Control (CBAC) ACLs
Types of ACLs

## Slide 23
Establish a Network Baseline .
Troubleshooting Methodologies and Troubleshooting Tools.
Common Issues that Occur During WAN Implementation.
Troubleshoot Common Inter-VLAN Connectivity Issues.
Troubleshoot Common Software or Hardware Misconfigurations Associated with VLANs.
Troubleshoot Enterprise Network Implementation Issues.
Troubleshooting

## Slide 24
Explain the importance of network documentation Network Baseline.
Establish a Network Baseline

## Slide 25
Describe the stages of the network documentation process.
Establish a Network Baseline (Cont.)

## Slide 26
Explain the purpose for measuring normal network performance when creating a baseline:
Establish a Network Baseline (Cont.)

## Slide 27
Describe how layered models, such as the OSI reference model or TCP/IP model, are used for troubleshooting.
Troubleshooting Methodologies and Troubleshooting Tools (Cont.)

## Slide 28
Describe the three stages of the general troubleshooting process.
Troubleshooting Methodologies and Troubleshooting Tools (Cont.)

## Slide 29
Describe the stages for gathering symptoms for troubleshooting a network problem.
Troubleshooting Methodologies and Troubleshooting Tools (Cont.)

## Slide 30
Describe the types of software tools that are commonly used when troubleshooting networks:
Software troubleshooting tools:
    Cisco view, 2. Solar winds, 3. HP Open view
Describe the types of hardware tools that are commonly used when troubleshooting networks.
Hardware troubleshooting tools are:
  1. Network analysis mode 2. Digital multi-meters
  3. Cable testers 4. Network analyzer
Secure Shell (SSH) Connections

## Slide 31
Describe the steps for designing or modifying a WAN.
Common Issues that Occur During WAN Implementation

## Slide 32
Describe common WAN implementation issues.
Common Issues that Occur During WAN Implementation (Cont.)

## Slide 33
Describe the common switch configuration Issues.
Troubleshoot Common Inter-VLAN Connectivity Issues

## Slide 34
Describe the common problems with VLANs and trunks.
Troubleshoot Common Software or Hardware Misconfigurations Associated with VLANs

## Slide 35
Describe how to troubleshoot network problems occurring at the physical layer.
Troubleshoot Enterprise Network Implementation Issues

## Slide 36
Describe how to troubleshoot network problems occurring at the data link layer.
Troubleshoot Enterprise Network Implementation Issues (Cont.)

## Slide 37
Describe how to troubleshoot network problems occurring at the network layer.
Troubleshoot Enterprise Network Implementation Issues (Cont.)

## Slide 38
Describe how to troubleshoot network problems occurring at the transport layer.
Troubleshoot Enterprise Network Implementation Issues (Cont.)

## Slide 39
Describe how to troubleshoot network problems occurring in the application layers.
Troubleshoot Enterprise Network Implementation Issues (Cont.)

## Slide 40
END