## Slide 1: IP Addressing and Subnetting

## Slide 2: IP Addressing
An IP address is a 32-bit sequence of 1s and 0s.
To make the IP address easier to use, the address is usually written as four decimal numbers separated by periods (dotted decimal format).

## Slide 3: IPV4 and IPV6

## Slide 4: Decimal and Binary Conversion

## Slide 5: IP V4 Addressing

## Slide 6: Two Parts: Network and Host
To define the network and host portions of an address, a devices use a separate 32-bit pattern called a subnet mask
The subnet mask does not actually contain the network or host portion of an IPv4 address, it just says where to look for network Part in a given IPv4 address
Notes: Section 8.1.2.1

## Slide 7: Bit-wise AND Operation
1 AND 1 = 1 1 AND 0 = 0 0 AND 1 = 0 0 AND 0 = 0
Notes: Section 8.1.2.5 and 8.1.2.6

## Slide 8: Reserved IP Addresses
Certain host addresses are reserved and cannot be assigned to devices on a network.
An IP address that has binary 0s in all host bit positions is reserved for the network address.
An IP address that has binary 1s in all host bit positions is reserved for the broadcast address.

## Slide 9: Network Address

## Slide 10: Broadcast Address

## Slide 11: Practice Problem
You have the IP address 176.89.21.201
Find the followings:
i) the subnet mask,
ii) network address
iii) broadcast address
iv) first host address and last host address of given IP.
v) Determine the no. of usable host

## Slide 12: Public and Private IP Addresses
No two machines that connect to a public network can have the same IP address because public IP addresses are global and standardized.
Assigned by the Internet Assigned Numbers Authority (IANA).
Private networks that are not connected to the Internet may use any host addresses, as long as each host within the private network is unique.
Connecting a network using private addresses to the Internet requires translation of the private addresses to public addresses using Network Address Translation (NAT).

## Slide 13: Connection between Private and Public IP Address

## Slide 14: Public and Private IP Addresses (contd.)
Private IP addresses can be intermixed with public IP addresses. This will conserve the number of addresses used for internal connections.

## Slide 15: Public Vs Private IP Addressess

## Slide 16: Introduction to Subnetting
To create a subnet address, a network administrator borrows bits from the host field and designates them as the subnet field.
IP Address

## Slide 17: Reasons for Subnetting
Large networks need to be segmented into smaller sub-networks, creating smaller groups of devices and services in order to:
Control traffic by containing broadcast traffic within subnetwork
Reduce overall network traffic and improve network performance
Subnetting - process of segmenting a network into multiple smaller network spaces called subnetworks or Subnets.
Communication Between Subnets
A router is necessary for devices on different networks and subnets to communicate.
Each router interface must have an IPv4 host address that belongs to the network or subnet that the router interface is connected to.
Devices on a network and subnet use the router interface attached to their LAN as their default gateway.
Notes: 9.1 Subnetting an IPv4 Network
9.1.1 Network Segmentation
9.1.1.1 Reasons for Subnetting
9.1.1.2 Communication Between Subnets

## Slide 18: Practice Problem
You have the IP address 176.89.21.201, this network is subnetted by 9 bits.
Find the followings:
i) the subnet mask, network address, broadcast address, first host address and last host address of given IP.
ii) Determine the no. of subnet and no. of usable host per subnet.
iii) Determine the available IP range of subnet number 126
iv) To which subnet and host number the following IP belong to: 176.89.201.101

## Slide 19: Examining Prefix (Slash Notation)
Notes: Section 8.1.2.2

## Slide 20: Subnets in Use
Subnet 0
Network 192.168.1.0-127/25
Subnet 1
Network 192.168.1.128-255/25
Notes: 9.1.3.2 Subnets in Use

## Slide 21: Subnetting based on Host Requirements
There are two considerations when planning subnets:
Number of Subnets required
Number of Host addresses required
Formula to determine number of useable hosts
  2^n-2
  2^n (where n is the number of host bits remaining) is used to calculate the number of hosts
  -2 Subnetwork ID and broadcast address cannot be used on each subnet
Notes: 9.1.4 Determining the Subnet Mask
9.1.4.1 Subnetting based on Host Requirements

## Slide 22: Magic Formulas
Number of Usable Hosts/Subnet
2h-n – 2
28-0- 2 = 256 - 2 = 254
28-1- 2 = 128 - 2 = 126
28-2- 2 = 64 - 2 = 62
28-3- 2 = 32 - 2 = 30
n = # borrowed bits
h = # bits available in host address
Number of Usable Subnets
2n
20 = 1
21 = 2
22 = 4
23 = 8

## Slide 23: Example: Creating 8 Subnets
Borrowing 3 bits to Create 8 Subnets. 23 = 8 subnets
Notes: 9.1.3.5 Creating 8 subnets

## Slide 24: Example: Creating 8 Subnets ( contd. )
Notes: 9.1.3.5 Creating 8 Subnets (continued)

## Slide 25: Set Up Subnets
200.200.200.10
5 Subnets
What is the Subnet Mask?
What are the Network Addresses?
What is the Broadcast Domain
What IP Addresses are available?

## Slide 26: Example – 1
128.16.32.13
What is the Subnet Mask?
What are the Network Addresses?
What is the Broadcast Domain
What IP Addresses are available?
* Needs 500 Subnets

## Slide 27: Example – 2
175.116.23.13/21
What is the Subnet Mask?
What are the Network Addresses?
What is the Broadcast Domain
What IP Addresses are available?
Subnet:
  At least 500 host/subnet
175.116.200.15?
?
?
?
?

## Slide 28: Questions????