## Slide 1: Frictional Properties
Mousumi Rahaman Hashi
Senior Lecturer
Dept. of Textile Engineering
Faculty of Engineering

## Slide 2: Frictional Properties
Friction is the force that resists the movement of a surface over another surface during sliding. When fibres are processed in textile industry, friction is developed between them. Due to the friction, the properties shown by textile fibres are called as frictional properties.

## Slide 3: Factors affecting the frictional intensity of textile materials:
Composition of the material (natural/synthetic)
The state of the surface (slippery/rough surface)
Pressure between two surfaces
Area of contact or angle of contact
Speed of sliding of one surface over another
Temperature
Water absorption of fiber

## Slide 4: Directional Frictional Effect (DFE):
The friction of the wool fiber depends on the direction in which it is pulled. The resistance is greater when it is pulled against the scales than when it is pulled with the scales. This is known as the directional frictional effect. So, in case of wool fiber it can be said that, less friction takes place between the fibers with the direction of scales and the friction becomes higher between the fibers against the scales.

## Slide 5: Co-efficient of friction
Frictional intensity of textile fibers can be determined by measuring co-efficient of friction. According to the 2nd law of friction, frictional force is proportional to the perpendicular force of a material due to its own weight.
So, F ∞ N; where F= Frictional force & N= Normal or perpendicular force
Or, F= µ N
Or, µ= F/N
Here, µ is the proportionate constant known as co-efficient of friction. Thus, co-efficient of friction can also be defined as the ratio between frictional force and perpendicular force of a material.

## Slide 6: Importance of friction in Textile Industry
Friction holds the fiber in a sliver and hence material does not break due to self weight.
Friction helps in drafting and drawing process.
Uniform tension can be maintained in winding and warping because of friction.
Friction helps in twisting during spinning.
Friction modifies the lustre and appearance of a cloth
Friction makes more clean yarn.

## Slide 7: Problems of friction in Textile Industry
Friction causes neps formation.
Over friction causes high breakage of yarn in weaving.
Due to friction handle properties of fabric will be changed.
Sometimes, due to friction textile materials may be elongated.
Friction causes yarn and fabric hairiness.
Friction causes static charge formation in textile material and therefore, dust, dirt etc. are attracted by the textile material and it becomes dirty.
Friction worns out different parts of a machine.

## Slide 8: Minimization of frictional intensity of textile materials
Sizing is done on warp yarn before weaving to reduce friction between adjacent yarns, as a result ends breakage rate during weaving becomes minimized.
Emulsion, oil, lubricants etc. are applied specially on jute in batching section to reduce the stiffness of fiber and thus fiber damage is reduced in processing.
Chemical treatment is applied on wool fiber to reduce scale sharpness and thus frictional intensity of fiber is minimized.
By calendaring it is possible to minimize the frictional intensity of cloth.
Sometimes resin finish or anti-crease finish can be applied on cloth to reduce the frictional intensity.
Softener can also be applied on textile material to reduce it’s frictional intensity.

## Slide 9: Laws of friction
The frictional force is independent of the area of contact between two surfaces.
The frictional force `F’ is proportional to the normal reaction `RN’. So, the Co-efficient of friction comes-
So, F∞ N; where F= Frictional force & N= Normal or perpendicular force
Or, F= µ N
Or, µ= F/N
This law is known as Coulomb’s law and friction’s 3rd law. Kinetic force is independent of the speed of sliding.

## Slide 10: Amonton’s law of friction

## Slide 11: Amonton’s law of friction
Measurement of co-efficient of friction:
Capstan method is very popular and commonly used to determine the co-efficient of friction. Two methods are involved:-
Static Capstan method
Dynamic Capstan method.

## Slide 12: Static Capstan Method
Capstan method is more convenient for the rapid technical evaluation of frictional resistance. The co-efficient of friction assumed to be constant, can be calculated from the relation.
Now From Amonton’s low,
T2/T1=
Taking log in both sides,
LogT2/T1=µө
=>µ= 1/Ɵ logT2/T1
=>µ= 1/π logT2/T1, Here ө= Angle of contact= π

## Slide 13: Dynamic Capstan Method
When a yarn is running continuously over a guide, then this method is suitable and most commonly used. Here, the tension is measured by tension meter which measure electrically with resistance, capacitance or inductance. Reducing of weight is not necessary here.
Now, by Amonton’s law,

## Slide 14: Types of frictions in fiber
Inter fiber friction.
Fiber-Non fiber friction.

## Slide 15: Frictional Intensity can be minimized
1. By processing with lubricates
Lubricating material as emulsion is used before jute spinning. Sizing is done during weaving preparation process. It also reduces yarn damage. Emulsion, oil, lubricants are applied specially on Jute fiber to reduce friction.
2. by chemical treatment:
By using acid or alkali. Acid or alkali is done on wool fiber to reduce scale sharpness and thus frictional intensity.
3. by finishing process:
a. Mechanical finishing- Ironing of calendaring.
b. Chemical finishing: By using resin. Resin is one typed anti-crease agent because it prevents fiber from creasing by blocking hydroxyl groups.
By using softener we can minimize frictional intensity.

## Slide 16: Measurement of friction
Methods of friction measurement can be divided into two classes.
1. Friction at only one point of contact.
a. Between two identical fibers.
b. Between two different fibers.
c. Between a fiber and non-fiber materials such as metal, plastic and ceramic.
2. Average friction at a great number of contacts.

## Slide 17
Thank You All