## Slide 1: PYSICAL STUCTURES OF FIBRE
Mousumi Rahaman Hashi
Senior Lecturer
Dept. of Textile Engineering
Faculty of Engineering

## Slide 2: Requirement of fiber formation or fiber forming polymer
1) Polymer should have long & linear chain molecules.
2) They must be chemically resistance.
3) Molecular chain must be parallel to each other.
4) They should have attractions.
5) Some measures of freedoms of molecules movement due to give required extensibility.
6) Lateral forces to hold the molecules together and gives cohesion the structure.

## Slide 3: Methods of fiber structure investigation
1) X-ray diffraction method
2) Infra-red radiation method
3) Electron microscopic method
4) Optical microscopic method
5) Thermal analysis
6) Nuclear magnetic resonance methods
7) Density

## Slide 4: Properties of x-ray diffraction method
1) Determination of chemical groups
2) Determination of molecular spacing
3) Determination of chemical bonding
4) Determination of degree of crystallinity & orientation
5) Determination of water absorption

## Slide 5: Properties of Infra- red radiation absorption method
1) Determination of spiral turns or convolution of cotton fiber
2) Determination of molecular spacing
3) Determination of chemical bonding
4) Determination of degree of crystallinity & orientation
5) Determination of molecular packing
6) Determination of cross-sectional shape of fiber
7) Identifications of fiber

## Slide 6
Crystallinity:
Crystallinity is the arrangement of fiber molecules in the molecular chain.
Properties of crystallinity:
1) More dense
2) More stiff
3) More strength
4) More rigid
5) Less water absorbent
Measurement of crystallinity:
1) X-ray diffraction method
2) Infra-red radiation absorption method
3) Density measurement methods

## Slide 7: Orientation
Orientation is the arrangement of molecular chain of fiber.
Properties of Orientation:
1) More dense 5) Less water absorbent
2) More stiff 6) More lustrous
3) More strength 7) Less elastic as less extension
4) More rigid
Measurement of Orientation:
1) X-ray diffraction method
2) Infra-red radiation absorption method
3) Density measurement methods

## Slide 8: Effects of structural factors on fiber properties
Chemical bonding:
a)Double bond
More strength, less flexibility
b) Single bond
Less strength, more flexibility

## Slide 9: Effects of structural factors on fiber properties
Character of polymer chain:
a) Long chain, such as [-CH2-CH2-CH2-CH2-CH2-CH2-]n
More strength, less flexibility
b) Short chain, such as [-CH2-CH2-]n
Les strength, more flexibility
c) Long side chain
More strength, less flexibility
d) Short side chain
Less strength, more flexibility

## Slide 10: Effects of structural factors on fiber properties
Molecular packing:
a) Regular packing:
CH3 CH3
׀ ׀
CH2-C-CH2-C-CH2
׀ ׀
CH3 CH3
-More strength, less flexibility
b) Irregular packing:
CH3
׀
N H-C-H
׀ ׀
-CH2-C-CH2-C-CH2-
׀ ׀
CH3 CH3
-Less strength, more flexibility

## Slide 11
Crystallinity:
High crystalline, higher strength and less flexibility
Orientation:
High Orientation, higher strength and less flexibility
Nature of Monomer:
a) Same monomer (Homo polymer)
More strength, less flexibility
b) Different monomer (Co-polymer)
Less strength, more flexibility
Internal structure of fiber polymer:
a) For ring structure
More strength, less flexibility
b) For normal structure
Less strength, more flexibility

## Slide 12
Thanks All