## Slide 1
Digital Communication
Digital Communication is that where the message or data is in digital form of
signal, then the digital message signal is modulated by using digital modulation techniques
Then transmitted by transmitter.
So
1.What is the basic Difference between Digital and Analog Communication System?
2.What is Analog Signal?
3.What is Digital Signal?
4.What is Digital Modulation ? And what are the techniques?
5.What are the Differences between Digital and Analog Modulation Techniques?
6.Actually message signals from input transducer (microphone ,camera or Keyboard are what types ?
Analog or Digital?
7.If Analog how can we convert this into digital in Digital communication?

## Slide 2
An analog signal signifies a continuous signal that keeps changes with a time period.
A digital signal signifies a discrete signal that carries binary data and has discrete values.
Analog signals are continuous sine waves. Digital signal is square waves.

## Slide 4
Basic Difference between Digital and Analog Communication System
Analog communication uses analog signal whose amplitude varies continuously with time from 0 to infinite. Digital communication uses digital signal whose amplitude is of two levels either Low i.e., 0 or either High i.e., 1.
Advantages of Digital Communication
Digital circuits are more reliable.
Digital circuits are easy to design and cheaper than analog circuits.
The configuring process of digital signals is easier than analog signals.
Digital signals can be saved and retrieved more conveniently than analog signals.

## Slide 7
A/D
Converter
Channel Encoder
Modulator
[Input signal]
Analog or continuous signal
Digital Bit
Digital signal pulse
Digital Modulated
signal
Digital Message signal
and
Carrier signal
Digital Communication (Digital Transmitter)
A/D Converter: Analog To Digital Converter

## Slide 8
LPF
Sampler
Quantizer
Bit Encoder
Digital Signal
Discreet Signal
Analogue Signal
Quantized Signal
c
c
c
Analogue Signal
Analog to Digital (A/D) Conversion:
PCM technic (pulse code modulation):-

## Slide 9
A/D Conversion and Sampling Theorem

## Slide 12
11
10
9
8
7
6
5
4
3
2
1
o
0 1 2 3 4 5 6 7
6
8 9 10 11 12
Discreet Signal and Quantized Signal
Analogue Message Signal
v
We know..
v=2mp/L
Where,
L=Number of quantization level
v=Quantization interval
Here L=2n
n = Number of Bit to represent Each quantized Sample
mp
Sample | Level | Digital
X(0) | 6 | 0110
X(1) | 8 | 1000
X(2) | 9 | 1001
X(3) | 10 | 1010
X(4) | 11 | 1011
X(5) | 10 | 1010
X(6) | 9 | 1001
X(7) | 8 | 1000
X(8) | 4 | 0100
X(9) | 3 | 0011
X(10) | 2 | 0010
X(11) | 3 | 0011
X(12) | 4 | 0100
mp
1 Sec

## Slide 13
L | Binary Code | Digital pulse
0 | 0000 | 
1 | 0001 | 
2 | 0010 | 
3 | 0011 | 
4 | 0100 | 
5 | 0101 | 
6 | 0110 | 
7 | 0111 | 
8 | 1000 | 
9 | 1001 | 
1o | 1010 | 
11 | 1011 | 
Digital pulse of Binary Code:-

## Slide 15
Sample | Level | Digital
X(0) | 6 | 0110
X(1) | 8 | 1000
X(2) | 9 | 1001
X(3) | 10 | 1010
X(4) | 11 | 1011
X(5) | 10 | 1010
X(6) | 9 | 1001
X(7) | 8 | 1000
X(8) | 4 | 0100
X(9) | 3 | 0011
X(10) | 2 | 0010
X(11) | 3 | 0011
X(12) | 4 | 0100
0110100010011010………………

## Slide 16: A television signal has a bandwidth of 4.5MHz.This signal is sampled quantized and binary coded to obtain PCM signal. 1.Determine sampling rate if the signal is sampled at a rate 20% above the normal sampling rate. 2.Determine binary pulse rate in Kbps if the sample is quantized into 1024 level.
We know..
v=2mp/L
Where,
L=Number of quantization level
v=Quantization interval
Here L=1124

## Slide 17: Solution:-
Ans:
1) Sampling rate = {(4.5x106) x2} +2(4.5x106) x0.2
=10.8x106 sample/sec
2)Total bit = 10.8x106x10
=10.8x107 bps
=10.8x104 Kbps
=108x103 Kbps
=108 Mbps

## Slide 18
Quantization Error and Quantization Noise
Ref. Book-Modern-Digital-And-Analog-Communication-Systems-4th-edition-by-Lathi
Chp.6 Quantization Error and Quantization Noise