## Slide 1: Digital Data Representation and Data Transmission

## Slide 2
Digital Data Transmission Mode
Parallel Transmission
Serial Transmission
Synchronous Transmission
Asynchronous Transmission

## Slide 3: PARALLEL TRANSMISSION: Multiple bits are send using one clock trick. Generally 1 byte data is send at a time.
SENDER
RECEIVER
01101011
Need 8 line
8 bit data at a time
Used in computer internal data transmission.
Generally,
PC to printer
PC to Modem
PC to Pendrive

## Slide 4: Serial Transmission: 1 bit data send in each clock trick.
SENDER
RECEIVER
0 1 0 0 1 1 1 0 0
Serial Transmission

## Slide 5: Asynchronous Transmission: We send 1 start bit (0) at the beginning and one stop bit (1) at the end of each byte and a gape between each byte is kept.
SENDER
RECEIVER
01 0 0 0 1 1 0 0 1 01 0 0 1 1 1 1 0 1
Start bit
Stop bit
Stop bit
Start bit
Gap between two byte
Slow data transmission rate for extra synchronous bits

## Slide 6: Synchronous Transmission: We send data bit one after another without sending start bit and stop bit . The responsibility of the receiver to group the bits.
SENDER
RECEIVER
0 1 0 0 1 1 1 0 1 0 1 0 0 0 1 1 1 0 0 1
2 group
1 byte

## Slide 7: Digital Data Representation or Line Coding:
RZ Return to zero
NRZ Non Return to zero
RZ
Bipolar RZ
On-Off RZ
Polar RZ

## Slide 8: ON-OFF RZ :
0 1 1 1 0 0 1 1
ON-OFF NRZ :
0 1 1 1 0 0 1 1

## Slide 9: Polar RZ :
0 1 1 1 0 0 1 1
Polar NRZ:
0 1 1 1 0 0 1 1

## Slide 10: Bipolar RZ:
0 1 1 1 0 0 1 1