## Slide 1: Introduction to Assembly language

## Slide 2: What is an assembly language?
Assembly language is a low level programming language. You need to get some knowledge about computer structure in order to understand anything.
The simple computer model as I see it:

## Slide 3: What is an assembly language?
The system bus (shown in yellow) connects the various components of a computer.
The CPU is the heart of the computer, most of computations occur inside the CPU.
RAM is a place to where the programs are loaded in order to be executed.

## Slide 4: Inside the CPU

## Slide 5: General Purpose Registers
8086 CPU has 8 general purpose registers, each register has its own name:
AX - the accumulator register (divided into AH / AL).
BX - the base address register (divided into BH / BL).
CX - the count register (divided into CH / CL).
DX - the data register (divided into DH / DL).
SI - source index register.
DI - destination index register.
BP - base pointer.
SP - stack pointer.
[N.B. The size of the above registers is 16 bit]

## Slide 6: General Purpose Registers
4 general purpose registers (AX, BX, CX, DX) are made of two separate 8 bit registers. For example,
if AX = 0011000000111001b,
then AH = 00110000b and AL = 00111001b.
Therefore, when you modify any of the 8 bit registers 16 bit register is also updated, and vice-versa.
The same is for other 3 registers, "H" is for high and "L" is for low part.

## Slide 7: Segment & Special Purpose Registers
CS - points at the segment containing the current program.
DS - generally points at segment where variables are defined.
ES - extra segment register, it's up to a coder to define its usage.
SS - points at the segment containing the stack.
IP - the instruction pointer.
Flags Register - determines the current state of the processor.

## Slide 8: Variables
Variable is a memory location.
It is much easier to have some value be kept in a variable named "var1" then at the address 5A73:235B, especially when you have 10 or more variables.
    DB - stays for Define byte(s).‏
    DW - stays for Define word(s)‏.
    DD - stays for Define double word(s)‏.
    DQ - stays for Define quad word(s)‏.
Syntax for a variable declaration:-
  name DB value
  name DW value

## Slide 9: Defining Data
Numeric data values
  100 - decimal
  100B - binary
  100H - hexadecimal
  '100' - ASCII
  "100" - ASCII

## Slide 10: Data Transfer Instructions
MOV target, source
  reg, reg
  mem, reg
  reg, mem
  mem, immed
  reg, immed
Sizes of both operands must be the same.
reg can be any non-segment register except IP cannot be the target register.

## Slide 11: Memory Models
.Model memory_model
  tiny: code+data <= 64K (.com program)‏
  small: code<=64K, data<=64K, one of each
  medium: data<=64K, one data segment
  compact: code<=64K, one code segment
  large: multiple code and data segments
  huge: allows individual arrays to exceed 64K

## Slide 12: Program Structure
.MODEL…. // selects a standard memory model for the programs.
.STACK 100H //sets the size of the program stack which may b any size up to 64kb
.DATA // all variables pertaining to the program are defined in the area.
.CODE // identifies the part of the program that contains instructions. MAIN PROC //creates a name and a address for the beginning of a procedure.
……………. define main procedures.
…………….
MAIN ENDP // indicates the end of the procedure.
END MAIN // terminates assembly of the program.

## Slide 13: Example (Print Hello World!)
.MODEL SMALL
.STACK 100H
.DATA
message db “Hello World! $” ; Message to be displayed
.CODE
MAIN PROC
mov ax,@data
mov ds,ax
mov ah,9h ; function to display a string
mov dx,offset message ; offset of Message string
int 21h ; Dos Interrupt (initiate the process)
mov ax,4C00h ; function to terminate
int 21h ; Dos Interrupt
MAIN ENDP
END MAIN

## Slide 14
The End