## Slide 1: Flexural Properties
Chapter 02

## Slide 2: What is Flexural Properties?
The behaviors shown by textile materials (fibre, yarn and fabric), when it is subjected to bending, are known as flexural properties.

## Slide 3: Flexural rigidity
Flexural rigidity is the resistance of a textile fibre against bending.
The unit of flexural rigidity is N-mm2, N-m2 etc.
Mathematically, Flexural rigidity, Rf = x
Where,
η = Shape factor
Е = Specific shear modulus (in N/tex)
T = Linear density (in tex)
ρ = Density (in gram/cm3)

## Slide 4: Specific Flexural rigidity
The specific flexural rigidity is the flexural rigidity of a textile fibre of unit linear density. Specific flexural rigidity is usually expressed as N-mm2/tex, N-m2/tex etc.
Mathematically, Specific Flexural rigidity = x
Where,
η = Shape factor
Е = Specific shear modulus (in N/tex)
T = Linear density (in tex)
ρ = Density (in gram/cm3)

## Slide 5: Bending recovery
The power of recovery from an immediate curvature of textile fibre is known as bending recovery.
For example, nylon of 15 denier shows 100% recovery from a small curvature, whereas only 20% recovery is obtained from a large curvature

## Slide 6: Bending modulus
Bending modulus can be defined as the ratio between bending stress and bending strain. Here, bending strain is usually expressed as degree or radian.
So, Bending modulus =

## Slide 7: Shape factor
Shape factor is a quantity or number that indicates the thickness or cross-section of a fibre. Shape factor is usually expressed by η.
If η =1, then the fibre is round shaped.
If η >1, then the fibre thickness is increased.
If η <1, then the fibre thickness is reduced.

## Slide 8: Shape factor of different fibres
Fibre | Shape factor | Fibre | Shape factor
Viscose | 0.74 | Acetate | 0.67
Wool | 0.80 | Nylon | 0.91
Silk | 0.59 | Glass | 1.0

## Slide 9: Thank You