## Slide 1: Information Theory & Coding
Huffman and Entropy Coding
Professor Dr. A.K.M Fazlul Haque
Electronics and Telecommunication Engineering (ETE)
Daffodil International University

## Slide 2
Note:
Fixed-length encoding
  ASCII, Unicode
Variable-length encoding : assign longer code words to less frequent characters, shorter code words to more frequent characters.
Basic Idea

## Slide 3: Huffman Coding
Huffman codes can be used to compress information
  Like WinZip – although WinZip doesn’t use the Huffman algorithm
  JPEGs do use Huffman as part of their compression process

## Slide 4
As an example, lets take the string:
  “duke blue devils”
We first to a frequency count of the characters:
    e:3, d:2, u:2, l:2, space:2, k:1, b:1, v:1, i:1, s:1
Next we use a Greedy algorithm to build up a Huffman Tree
  We start with nodes for each character
e,3
d,2
u,2
l,2
sp,2
k,1
b,1
v,1
i,1
s,1
Huffman Coding (Cont.)

## Slide 5
We then pick the nodes with the smallest frequency and combine them together to form a new node.
  The selection of these nodes is the Greedy part
The two selected nodes are removed from the set, but replace by the combined node.
This continues until we have only 1 node left in the set.
Huffman Coding (Cont.)

## Slide 6
e,3
d,2
u,2
l,2
sp,2
k,1
b,1
v,1
i,1
s,1
Huffman Coding (Cont.)

## Slide 7
e,3
d,2
u,2
l,2
sp,2
k,1
b,1
v,1
i,1
s,1
2
Huffman Coding (Cont.)

## Slide 8
e,3
d,2
u,2
l,2
sp,2
k,1
b,1
v,1
i,1
s,1
2
2
Huffman Coding (Cont.)

## Slide 9
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
Huffman Coding (Cont.)

## Slide 10
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
4
Huffman Coding (Cont.)

## Slide 11
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
4
4
Huffman Coding (Cont.)

## Slide 12
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
4
4
5
Huffman Coding (Cont.)

## Slide 13
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
4
4
5
7
Huffman Coding (Cont.)

## Slide 14
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
4
4
5
7
9
Huffman Coding (Cont.)

## Slide 15
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
4
4
5
7
9
16
Huffman Coding (Cont.)

## Slide 16
Now we assign codes to the tree by placing a 0 on every left branch and a 1 on every right branch.
A traversal of the tree from root to leaf give the Huffman code for that particular leaf character.
Note that no code is the prefix of another code.
Huffman Coding (Cont.)

## Slide 17
e,3
d,2
u,2
l,2
sp,2
k,1
i,1
s,1
2
b,1
v,1
2
3
4
4
5
7
9
16
0
1
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
e | 00
d | 010
u | 011
l | 100
sp | 101
i | 1100
s | 1101
k | 1110
b | 11110
v | 11111
1
Huffman Coding (Cont.)

## Slide 18
These codes are then used to encode the string.
Thus, “duke blue devils” turns into:
010 011 1110 00 101 11110 100 011 00 101 010 00 11111 1100 100 1101
When grouped into 8-bit bytes:
01001111 10001011 11101000 11001010 10001111 11100100 1101xxxx
Thus it takes 7 bytes of space compared to 16 characters * 1 byte/char = 16 bytes uncompressed
Huffman Coding (Cont.)

## Slide 19
Uncompressing works by reading in the file bit by bit.
  Start at the root of the tree
  If a 0 is read, head left
  If a 1 is read, head right
  When a leaf is reached decode that character and start over again at the root of the tree
Thus, we need to save Huffman table information as a header in the compressed file.
  Doesn’t add a significant amount of size to the file for large files (which are the ones you want to compress anyway)
  Or we could use a fixed universal set of codes/freqencies
Huffman Coding

## Slide 20: Most important properties of Huffman Coding
  Unique Prefix Property: No Huffman code is a prefix of any other Huffman code
    For example, 101 and 1010 cannot be Huffman codes. Why?
  Optimality: The Huffman code is a minimum-redundancy code (given an accurate data model)
    The two least frequent symbols will have the same length for their Huffman code, whereas symbols occurring more frequently will have shorter Huffman codes
    It has been shown that the average code length of an information source S is strictly less than  + 1, i.e.
     l’ <  + 1

## Slide 21: Data Compression Scheme
Encoder
(compression)
Codes /
Code words
Storage or
Networks
Decoder
(decompression)
Output Data
Input Data
Codes /
Code words
B0 = # bits required before compression
B1 = # bits required after compression
Compression Ratio = B0 / B1.

## Slide 22: Compression Techniques
Coding Type | Basis Technique | 
Entropy Encoding | Run-length Coding | 
 | Huffman Coding | 
 | Arithmetic Coding | 
Source Coding | Prediction | DPCM
 |  | DM
 | Transformation | FFT
 |  | DCT
 | Layered Coding | Bit Position
 |  | Subsampling
 |  | Sub-band Coding
 | Vector Quantization | 
Hybrid Coding | JPEG | 
 | MPEG | 
 | H.263 | 
 | Many Proprietary Systems | 

## Slide 23: Compression Techniques (Cont.)
Entropy Coding
  Semantics of the information to encoded are ignored
  Lossless compression technique
  Can be used for different media regardless of their characteristics
Source Coding
  Takes into account the semantics of the information to be encoded.
  Often lossy compression technique
  Characteristics of medium are exploited
Hybrid Coding
  Most multimedia compression algorithms are hybrid techniques

## Slide 24: Entropy Encoding
Information theory is a discipline in applied mathematics involving the quantification of data with the goal of enabling as much data as possible to be reliably stored on a medium and/or communicated over a channel.
According to Claude E. Shannon, the entropy  (eta) of an information source with alphabet S = {s1, s2, ..., sn} is defined as
where pi is the probability that symbol si in S will occur.

## Slide 25: Entropy Encoding (Cont.)
Example 1: What is the entropy of an image with uniform distributions of gray-level intensities (i.e. pi = 1/256 for all i)?
Example 2: What is the entropy of an image whose histogram shows that one third of the pixels are dark and two thirds are bright?

## Slide 26: Entropy Encoding: Run-Length
Data often contains sequences of identical bytes. Replacing these repeated byte sequences with the number of occurrences reduces considerably the overall data size.
Many variations of RLE
  One form of RLE is to use a special marker M-byte that will indicate the number of occurrences of a character
    “c”!#
      How many bytes are used above? When do you think the M-byte should be used?
    ABCCCCCCCCDEFGGG
    is encoded as
    ABC!8DEFGGG
      What if the string contains the “!” character?
      How much is the compression ratio for this example

## Slide 27: 3.8 Entropy Encoding: Run-Length (Cont.)
Many variations of RLE :
  Zero-suppression: In this case, one character that is repeated very often is the only character used in the RLE. In this case, the M-byte and the number of additional occurrences are stored.
  When do you think the M-byte should be used, as opposed to using the regular representation without any encoding?

## Slide 28: Entropy Encoding: Run-Length (Cont.)
Many variations of RLE :
  If we are encoding black and white images (e.g. Faxes), one such version is as follows:
  (row#, col# run1 begin, col# run1 end, col# run2 begin, col# run2 end, ... , col# runk begin, col# runk end)
  (row#, col# run1 begin, col# run1 end, col# run2 begin, col# run2 end, ... , col# runr begin, col# runr end)
  ...
  (row#, col# run1 begin, col# run1 end, col# run2 begin, col# run2 end, ... , col# runs begin, col# runs end)

## Slide 29: Entropy Encoding: Huffman Coding
One form of variable length coding.
Greedy algorithm.
Has been used in fax machines, JPEG and MPEG.

## Slide 30: Entropy Encoding: Huffman Coding (Cont.)
Algorithm of Huffman Coding:
Input: A set C = {c1 , c2 , ... , cn} of n characters and their frequencies {f(c1) , f(c2 ) , ... , f(cn )}
Output: A Huffman tree (V, T) for C.
1. Insert all characters into a min-heap H according to their frequencies.
2. V = C; T = {}
3. for j = 1 to n – 1
4. c = deletemin(H)
5. c’ = deletemin(H)
f(v) = f(c) + f(c’) // v is a new node
Insert v into the minheap H
Add (v,c) and (v,c’) to tree T making c and c’ children of v in T
9. end for

## Slide 31
END