## Slide 1: Nuclear Power Plant
Prepared by-
Nusrat Chowdhury
Lecturer
Dept. of EEE
Daffodil International University (DIU)

## Slide 2: Introduction
A generating station in which nuclear energy is converted into electrical energy is known as a nuclear power station.
In nuclear power station, heavy elements such as Uranium (U235) or Thorium (Th232) are subjected to nuclear fission in a special apparatus known as a reactor.
The heat energy thus released is utilized in raising steam at high temperature and pressure.
The steam runs the steam turbine which converts steam energy into mechanical energy.
The turbine drives the alternator which converts mechanical energy into electrical energy

## Slide 3: Continue…
The most important feature of a nuclear power station is that huge amount of electrical energy can be produced from a relatively small amount of nuclear fuel as compared to other conventional types of power stations.
It has been found that complete fission of 1 kg of Uranium (U235) can produce as much energy as can be produced by the burning of 4,500 tons of high grade coal.
Although the recovery of principal nuclear fuels (i.e., Uranium and Thorium) is difficult and expensive,
yet the total energy content of the estimated world reserves of these fuels are considerably higher than those of conventional fuels, viz., coal, oil and gas.

## Slide 4: Advantages
The amount of fuel required is quite small. Therefore, there is a considerable saving in the cost of fuel transportation.
A nuclear power plant requires less space as compared to any other type of the same size.
It has low running charges as a small amount of fuel is used for producing bulk electrical energy.
This type of plant is very economical for producing bulk electric power.
It can be located near the load centers because it does not require large quantities of water and need not be near coal mines. Therefore, the cost of primary distribution is reduced.
There are large deposits of nuclear fuels available all over the world. Therefore, such plants can ensure continued supply of electrical energy for thousands of years.
It ensures reliability of operation.

## Slide 5: Disadvantages
The fuel used is expensive and is difficult to recover.
The capital cost on a nuclear plant is very high as compared to other types of plants.
The erection and commissioning of the plant requires greater technical know-how.
The fission by-products are generally radioactive and may cause a dangerous amount of radioactive pollution.
Maintenance charges are high due to lack of standardization. Moreover, high salaries of specially trained personnel employed to handle the plant further raise the cost.
Nuclear power plants are not well suited for varying loads as the reactor does not respond to the load fluctuations efficiently.
The disposal of the by-products, which are radioactive, is a big problem. They have either to be disposed off in a deep trench or in a sea away from sea-shore.

## Slide 6: FUSION AND FISSION

## Slide 7
Nuclear fission:
A large nucleus splits into several small nuclei when impacted by a neutron, and energy is released in this process
Nuclear fusion:
Several small nuclei fuse together and release energy.

## Slide 8: FUSION
DEUTERIUM
HELIUM
NEUTRON
http://fusioned.gat.com
TRITIUM
FUSION

## Slide 9: FISSION

## Slide 10: Energy Released By A Fission
235U + n --> fission + 2 or 3 n + 200MeV
Production of one molecule of CO2 in fossil fuel combustion only generates 4 eV or 6.5 x 10-19 j of energy
This is 50,000,000 times more energy
3.2 x 10-11 j
1MeV (million electron volts) = 1.609 x 10-13 j

## Slide 11
Fossil Fuel CO2 + 4 ev
235U + n --> fission + 2 or 3 n + 200 MeV
3.2 x 10-11 j
combustion
6.5 x 10 -19 j
(per U atom)
(per CO2 molec)
Energy Released By A Fission
50,000,000 times
more energy
1MeV (million electron volts) = 1.609 x 10-13 j

## Slide 12: The Fission of U-235

## Slide 13: Nuclear Chain Reaction
# fissions double every generation

## Slide 14
Nuclear Chain Reactions
Uncontrolled
Chain Reaction
Controlled
Chain Reaction
Bombs
Energy

## Slide 15: Radioactivity:
Alpha particle,α: An alpha particle is a radioactive particle that is made up of two protons and two neutrons. It is a helium nucleus: that is a helium atom without electrons. Radioactive elements give out alpha particles when they go through a kind of radioactive decay, known as alpha decay. Velocity of alpha particle is 1/10th of the speed of light.
Beta particle,β: A beta particle, also called beta ray or beta radiation, is a high-energy, high-speed electron or positron emitted by the radioactive decay of an atomic nucleus during the process of beta decay. There are two forms of beta decay, β− decay and β+ decay, which produce electrons and positron respectively.
Gamma particle,ϒ: A gamma ray or gamma radiation, is a penetrating electromagnetic radiation arising from the radioactive decay of atomic nuclei. It consists of the shortest wavelength electromagnetic waves and so imparts the highest photon energy.

## Slide 16: Half-Life
Half-life T1/2 : the time at which N is reduced to half of its initial value.
To calculate the value of half-life, we will use equation (4),
N(t) = N0e– λt
At half-life, T=T1/2 and N=N0 /2
So, N/N0 = e– λt1/2
0.5= e– λt1/2
So, we get,T1/2 = (ln2)/ λ
Or, T1/2 = 0.693/ λ
1.If the half-life of 100.0 grams of a radioactive isotope is 8 years, how many grams will remain in 32 years?
2. 300g of an substance decays to 112g after 180s. Determine half life of this substance?

## Slide 17: Fertile and Fissile material:
Fertile Material: Non-fissionable material from which fissionable material is generated by neutron absorption and subsequent nuclei conversions. Fertile materials are thorium-232 which can be converted into fissionable uranium-233, and uranium-238 which can be converted into fissionable plutonium-239.
Fissile Material: Fissile material, also called Fissionable Material, in nuclear physics, any species of atomic nucleus that can undergo the fission reaction. The principal fissile materials are uranium-235 (0.7 percent of naturally occurring uranium), plutonium-239, and uranium-233, the last two being artificially produced from the fertile materials uranium-238 and thorium-232, respectively.

## Slide 18: Mass Defect and Binding Energy:
Mass Defect: Proton and neutron are the constituent particles of nucleus. But the mass of a nucleus is found to differ from the sum of masses of proton and neutron .This difference in mass is known as mass defect.
The mass defect is given by the formula
Δm= (mn+mp) - mo
Here, (mn+mp) -represent combined mass of proton and neutron and mo- denotes original mass of atom
Binding Energy: The energy that holds a nucleus together. This is associated with the mass defect of the nucleus.
Nuclear binding energy = Δmc2

## Slide 19: Chain Reaction

## Slide 20: Schematic Arrangement of Nuclear Power Plant

## Slide 21: Continue….
The schematic arrangement of a nuclear power station is shown in Fig. The whole arrangement can be divided into the following main stages :
Nuclear reactor
Heat exchanger
Steam turbine
Alternator

## Slide 22: Nuclear Reactor
It is an apparatus in which nuclear fuel (U235) is subjected to nuclear fission. It controls the chain reaction* that starts once the fission is done. If the chain reaction is not controlled, the result will be an explosion due to the fast increase in the energy released.
A nuclear reactor is a cylindrical stout pressure vessel and houses fuel rods of Uranium, moderator and control rods.
The fuel rods constitute the fission material and release huge amount of energy when bombarded with slow moving neutrons.
The moderator consists of graphite rods which enclose the fuel rods. The moderator slows down the neutrons before they bombard the fuel rods.

## Slide 23: Continue….
The control rods are of cadmium and are inserted into the reactor. Cadmium is strong neutron absorber and thus regulates the supply of neutrons for fission. When the control rods are pushed in deep enough, they absorb most of fission neutrons and hence few are available for chain reaction which, therefore, stops.
However, as they are being withdrawn, more and more of these fission neutrons cause fission and hence the intensity of chain reaction (or heat produced) is increased.
Therefore, by pulling out the control rods, power of the nuclear reactor is increased, whereas by pushing them in, it is reduced. In actual practice, the lowering or raising of control rods is accomplished automatically according to the requirement of load. The heat produced in the reactor is removed by the coolant, generally a sodium metal. The coolant carries the heat to the heat exchanger.

## Slide 25
Heat exchanger. The coolant gives up heat to the heat exchanger which is utilized in raising the steam. After giving up heat, the coolant is again fed to the reactor.
Steam turbine. The steam produced in the heat exchanger is led to the steam turbine through a valve. After doing a useful work in the turbine, the steam is exhausted to condenser. The condenser condenses the steam which is fed to the heat exchanger through feed water pump.
Alternator. The steam turbine drives the alternator which converts mechanical energy into electrical energy. The output from the alternator is delivered to the bus-bars through transformer, circuit breakers and isolators.

## Slide 26: Coolant Cycles:
Coolant circulations from reactor to heat exchanger can be done by three ways:
Direct cycle: here coolant which is water leaves the reactor as steam. BWR uses this system.
Single Circuit System: Coolant transfers the heat to feed water in steam generator. PWR uses this system.
Double Circuit System: Two coolant; primary coolant after circulating through the reactor goes to heat exchanger and passes its heat to secondary coolant which transfers its heat to the feed water in steam generator. SGR and FBR uses this system.

## Slide 27: Coolant Cycles:

## Slide 28: Reactor Types:
Depending on neutron energy:
i)Fast reactor: non moderated neutrons are used
ii) Thermal or slow reactor: moderated or slow neutrons are used.
Depending on fuel:
i) U-235 ii) U-238 iii) Th-232
Depending on coolant:
Gas cooler reactor ii) Water cooler reactor iii) Liquid metal cooler reactor
Depending on moderator:
Graphite reactor ii) Beryllium reactor iii) Water reactor
Depending on core:
Homogeneous: Uniform mixture of fuel and moderator(aqueous mixture of Uranium salt)
Heterogeneous: Fuel rods inserted in moderator.

## Slide 29: Factors Affecting Design of Reactor:
Type of reactor
Type of fuel to be used
Power rating of reactor in MW
Coolant system
Control system
Rates of neutron production and absorption
Safety of reactor

## Slide 30: Boiling Water Reactor (BWR)
A boiling water reactor (BWR) uses demineralized water as a coolant and neutron moderator. Heat is produced by nuclear fission in the reactor core, and this causes the cooling water to boil, producing steam.
Enriched U-235 is used as fuel which contains more fissionable neutrons than normal condition.
Here, direct system is used for cooling, so water boils in reactor core.

## Slide 31: Pressurized Water Reactor (PWR)
The pressurized water reactor (PWR) is a type of nuclear reactor make use of light water(ordinary water, as opposed to heavy water) as their coolant and neutron moderator. Here coolant cycle is single circuit system.
Enriched U-235 is used as fuel which contains more fissionable neutrons than normal condition.
Pressure of 1200 p.s.i.g is given by pressurizer to remain water in liquid state.

## Slide 32: Sodium Graphite Reactor (SGR)
A nuclear reactor that uses slightly enriched uranium as fuel, graphite as moderator.
Its coolant cycle is double circuit system where Liquid sodium (Na) serves as the primary coolant and an alloy of sodium potassium (NaK) serves as the secondary coolant.

## Slide 33: Fast Breeder Reactor(FBR)
Under appropriate operating conditions, the neutrons given off by fission reactions can "breed" more fuel from otherwise non-fissionable isotopes. The most common breeding reaction is that of plutonium-239 from non-fissionable uranium-238. The term "fast breeder" refers to the types of configurations which can actually produce more fissionable fuel than they use. Uranium-238 is 140 times more abundant than the fissionable U-235 and can be efficiently converted into Pu-239 by the neutrons from a fission chain reaction.
In FBR, U-235 is covered with blanket of U-238 and no moderator is used. Its coolant cycle is double circuit system.

## Slide 34: Selection of Site for Nuclear Power Station
Availability of water
Disposal of waste
Distance from populated areas
Transportation facilities