## Slide 1: NFE 415 FOOD STORAGE ENGINEERING
Humyra Nowshin
Lecturer
Dept. of Nutrition & Food Engineering
Daffodil International University

## Slide 2: Lecture 8: Topic
Some Definitions
Fan Laws
The First Fan law
The Second Fan law
The Third Fan law
Why Should We Study These?

## Slide 3: Some Definitions
Fan
Turning machine that transmits energy to the fluid circulating inside it by increasing pressure.
Impeller
An impeller is a rotating component of a centrifugal pump which transfers energy from the motor that drives the pump to the fluid.
Volume
Volumetric flow related to a certain air density.

## Slide 4: Some Definitions (Contd.)
Static Pressure
Air pressure caused by its degree of compression ( What does it mean?) In the fan it is equivalent to the difference between the static outlet pressure and the total inlet pressure.
It can be positive or negative.
Dynamic Pressure
Air pressure caused by movement. In the fan it is equivalent to the average of the speeds at the outlet.
Dynamic pressure can only be positive.

## Slide 5: Some Definitions (Contd.)
Total Pressure
Air pressure owing to compression and movement. It is the algebraic addition of the dynamic and static pressures at a certain point.
Therefore, if the air is motionless, the total pressure equals the static pressure.

## Slide 6: Fan Laws
The Fan Laws are a group of useful equations for determining :
the effects of a change in the speed,
the diameter of the fan and
the density of air in the system
So, in short, the basic fan laws are used to express the relationship between fan performance and power.

## Slide 7: The First Fan law: Volume of Air
Volumetric flow rate (V, m³/hr) varies directly proportional to the ratio of the rotational speed (RPM)
V1/V2= RPM1/RPM2
Where:
Volume 1, m³/hr – Original volume of air
Volume 2, m³/hr – New Volume of air
RPM 1 – Original Speed
RPM 2 – New Speed

## Slide 8: The Second Fan Law: Pressure
Pressure (P, Pa) varies as the square to the ratio of the rotational speed (RPM) of the impeller
Where:
p2 =Pressure 2, Pa
p1 =Pressure 1, Pa
RPM 1 – Original Speed
RPM 2 – New Speed

## Slide 9: The Third Fan Law: Power
Power (P, kW) varies as the cube to the ratio of the rotational speed (RPM, u/min) of the impeller.
Where:
P1 =Power, kW2
P2 =Power, kW1
RPM 1 – Original Speed
RPM 2 – New Speed

## Slide 10: Why Should We Study These?
Although there are many fan selection software available in the marketplace, it is necessary for engineers to have at least a basic understanding of these basic fan laws to aid their overall awareness of how changes within ventilation systems can influence performance.

## Slide 11
THANK YOU