## Slide 1: Air property or PSYCHROMETRY
HUMYRA NOWSHIN
Lecturer
Department of Nutrition and Food Engineering
Daffodil International University

## Slide 2: OJECTIVE OF LECTURE
To Understand Psychrometric Properties.
To Understand Psychrometry Chart.
To Understand Psychrometry Processes.
To Understand Working Principle Of Airwasher

## Slide 3: Atmosphere

## Slide 4: What is Psychrometry
Psychrometry is the study of the properties of mixtures of dry air and water vapor
Example: how wet is the air ?
Why study psychrometry?
To be able to analyze various processes involving moist air.
Example: if the air is warm and wet, what will be the air-conditioning design required

## Slide 5: Important Psychrometric Properties
Dry Bulb Temperature (ºF or ºC)
Wet Bulb Temperature (ºF or ºC)
Humidity ratio (g / kg or Grains / lb)
Relative humidity (%)
Dew-point Temperature (ºF or ºC)
Specific volume (m3/kg, Cu. Ft/lb)
Enthalpy (KJ/Kg or Btu/lb)

## Slide 6: Dry Bulb Temperature (DBT)
 Dry bulb temperature (DBT) is the temperature of the moist air as measured by a standard thermometer or other temperature measuring instruments

## Slide 7: Wet Bulb Temperature
 Wet bulb temperature is the lowest temperature that can be reached by the evaporation of water only. It is the temperature one feels when one's skin is wet and is exposed to moving air.
The device has 2 thermometers.
One with a cotton wick saturated with water.

## Slide 8
Absolute humidity
The mass of water vapor per unit volume of air containing the water vapor. This quantity is also known as the water vapor density.

## Slide 9
Humidity Ratio / Specific Humidity
 The humidity ratio (or specific humidity) W is the mass of water associated with each kilogram of dry air. Assuming both water vapour and dry air to be perfect gases, the humidity ratio is given by:
mv – Mass of vapour
a
m – Mass of dry air
a
m
  mv
Units – g / kg or Grains / lb

## Slide 10: Relative Humidity
 The amount of moisture that air holds (mv) relative to the maximum amount of moisture the air can hold (ms) at the same temperature.
Relative humidity is normally expressed as a percentage. When Φ is 100 percent, the air is saturated.
ms
  mv

## Slide 11: Dew-Point Temperature
The temperature of saturated moist air at the same pressure and humidity ratio of a given air mixture.
This is the temperature at which condensation begins when the air is cooled at constant pressure
Example

## Slide 12: Specific Volume
The specific volume is defined as the number of cubic meters of moist air per kilogram of dry air.
Unit – m3/kg of dry air
Used to calculate mass flow rate of air

## Slide 13: Enthalpy
The enthalpy of moist air is the sum of the enthalpy of the dry air (Sensible heat) and the enthalpy of the water vapour(Latent Heat) .
Total Enthalpy = Sensible heat + Latent Heat
Sensible heat = Enthalpy due to change in temp.
Latent heat = Enthalpy due to change in humidity

## Slide 15: Psychrometry Chart
A Psychrometric chart is graphical representation of the thermodynamic properties of moist air.
Need two quantities for a state point
  Can get all other quantities from a state point
Can do all calculations without a chart
  Often require iteration
  Many “digital” psychrometric charts available

## Slide 16: Psychrometry Chart – Continue..

## Slide 17: Dry Bulb Temperature(DBT) Line

## Slide 18: Wet Bulb Temperature(WBT) Line

## Slide 19: Relative Humidity Lines

## Slide 20: Dew-Point Temperature Lines

## Slide 21: Humidity Ratio / Specific Humidity Lines

## Slide 22: Specific Enthalpy Lines

## Slide 23: Specific Volume Lines

## Slide 24: Psychrometric Processes
Sensible Heating
Sensible Cooling
Humidification
Dehumidification
Heating and Humidification
Cooling and Dehumidification
Cooling and Humidification
Heating and Dehumidification

## Slide 26
10
20
30
60 50 40
Relative humidity (%) 100 90 80 70
10
20
30
40
50
60
70
80
100
90
110
120
130
140
150
160
P1
P2
5 10 15 20 25 30 35 40 45 50 55 60 65 70 75 80 85 90 95 100 105 110 115 120 125 130 135
Enthalpy (kJ/kg) 0
-40 -35 -30 -25 -20 -15 -10 -5 0
Dry bulb temperature (°F)
0.0000
0.0050
0.0100
0.0150
0.0200
0.0250
0.0300
0.0350
0.0400
0.0450
Absolutehumidity (kg/kg)
Air at 44 ºF
Air at 65 ºF
Sensible Heating
Duct Heater

## Slide 27: Sensible Cooling Air at 65 ºF
10
20
30
60 50 40
Relative humidity (%) 100 90 80 70
0
Enthalpy (kJ/kg)
10
20
30
40
50
60
70
80
90
100
110
120
130
140
150
160
P1
P2
-5 0 5 10 15 20 25 30 35 40 45 50 55 60 65 70 75 80 85 90 95 100 105 110 115 120 125 130 135
-40 -35 -30 -25 -20 -15 -10
Dry bulb temperature (°F)
0.0000
0.0050
0.0100
0.0150
0.0200
0.0250
0.0300
0.0350
0.0400
0.0450
Absolutehumidity (kg/kg)
Air at 44 ºF
Cooling Coil
CHW in
CHW out

## Slide 29
Air at 57 ºF
Air at 75 ºF
Cooling Coil
CHW
in
CHW
out

## Slide 30: Cooling and Humidification

## Slide 33: Airwasher
An air washer is a device for conditioning air. In an air washer air comes in direct contact with a spray of water and there will be an exchange of heat and mass (water vapour) between air and water
The outlet condition of air depends upon the temperature of water sprayed in the air washer.
Hence, by controlling the water temperature externally, it is possible to control the outlet conditions of air, which then can be used for air conditioning purposes.

## Slide 35: QUESTIONS ???

## Slide 36: THANK YOU