## Slide 1: Fully Encased Composite Column (FECC)
Md. Abu Hasan
Senior Lecturer
Department of Civil Engineering
Daffodil International University.
Lecture On

## Slide 2: Fully Encased Composite Column
Introduction
FEC Column is a column composed of a steel shape core encased in
concrete with additional longitudinal reinforcing steel and lateral ties.
Lateral Ties/Stirrups
Structural shapes surrounded by concrete vertical and horizontal reinforcement to sustain encasement Shear connectors Can be used to help transfer forces
Longitudinal Bars

## Slide 3: Fully Encased Composite Column
Introduction
Difficult to
Place ?
Might use U-tie instead

## Slide 4: Fully Encased Composite Column
Properties
Concrete provides stiffening, strengthening,
fire and corrosion protection.
Steel Carries Construction load.
Might use when exposed concrete finish is desired.
Might use for transitions (concrete to steel columns)

## Slide 5: Fully Encased Composite Column
Properties
Flexural Stiffness governed by concrete
encasement.
Encasement prevents buckling of steel bars and steel shape.
Concrete outside ties crack and spalls, followed
by.
Might use for transitions (concrete to steel
columns) rest of encasement.
After spalling, post-yielding bucking of steel, overall failure.
Ref chenet. Al. 2014 Journal of Structural Engg. ASCE. March 2014

## Slide 6: Fully Encased Composite Column
AISC DESIGN PROVISIONS FOR COMPOSITE MEMBERS
Material Limitations
Concrete
Normal wt. concrete
Light wt. concrete
𝑐
21 𝑀𝑝𝑎 ≤ 𝑓′ ≤ 70 Mpa
𝑐
21 𝑀𝑝𝑎 ≤ 𝑓′ ≤ 42 Mpa
Structural Steel and Rebars
𝑓𝑦 ≤ 525 𝑀𝑝𝑎
Higher material strengths are permitted when their use is justified by testing or analysis.

## Slide 7: Fully Encased Composite Column
AISC DESIGN PROVISIONS FOR COMPOSITE MEMBERS
Design of composite sections requires consideration of both steel and concrete behavior .
The design, detailing and material properties related to the concrete and reinforcing steel portions shall comply with the reinforced concrete and reinforcing bar design specifications.
Resistance Prior to Composite Action
The factored resistance of the steel member prior to the attainment to composite action shall be determined in accordance with Steel Design Manual.

## Slide 8: Fully Encased Composite Column
AISC DESIGN PROVISIONS FOR COMPOSITE MEMBERS
Nominal Strength of Composite Sections
Plastic Stress Distribution Method
𝑐
𝑐
Nominal strength for steel is 𝐹𝑦 in either tension or compression.
Concrete components in compression reached a stress of 0.85 𝑓′
For round HSS filled with concrete, a stress of 0.95 𝑓′ Permitted.
Strain-Compatibility Method
A linear distribution of strains across the section shall be assumed , with the maximum concrete compressive strain = 0.03 mm/mm
The stress-strain relationships for steel and concrete shall be obtained from
tests or from published result for similar materials.

## Slide 9: Fully Encased Composite Column
AISC DESIGN PROVISIONS FOR COMPOSITE MEMBERS
Limitations for Encased Composite Column
1) Cross-Sectional area of steel must be at least 1% of total cross-section
continous
2) Concrete encasement must be reinforced with longitudinal bars and lateral ties/spirals-
-Transverse reinforcement ≥ 0.009 𝑖𝑛2/in
𝑨𝒔
𝑨
𝒈
≥ 𝟎. 𝟎𝟏
3) Reinforcement ratio must be at least 0.004
𝝆𝒔𝒓=0.004
𝑨𝒔
𝝆𝒔𝒓 = 𝑨
𝒈
Area of reinf. bars (𝑖𝑛2)
Gross area of composite member (𝑖𝑛2)

## Slide 10: Fully Encased Composite Column
AISC DESIGN PROVISIONS FOR FEC COLUMNS
Min. 1.5 𝑑𝑏, 1 − 1/2"Clear (between steel core and longitudinal reinf. bars)
Min. No. 3 @ 12" max
Or No. 4 @ 16" max
𝝆
𝒔𝒓
𝑨
= 𝒔𝒓
𝑨𝒈
𝝆𝒔𝒑
> _0.004
Area of rein f. bars (𝑖𝑛2)
Gross area of composite member (𝑖𝑛2)
Provisions of ACI 318 shall apply with exceptions and limitations (as listed in AISC 11.1), see ACI 318 Sections 7.10 and 10.9.3 for additional tie reinforcement provisions.
𝑆 ≤ 0.5 𝑑
Least column dimension
d

## Slide 11: Fully Encased Composite Column
AXIAL COMPRESSIVE STRENGTH FEC COLUMNS
Cross Section strength Po is the sum of axial load capacities of the materials that make up the cross section.
𝒄 𝒄
𝑷𝒐=𝑨𝒔𝑭𝒚 + 𝑨𝒔𝒓𝑭𝒚𝒓 + 𝟎. 𝟖𝟓 𝑨 𝒇′
−𝑷𝒐 = nominal elastic compressive strength without length effects
−𝑨𝒔 = area of steel section
−𝑨𝒔𝒓= area of continuous reinforcing bars
−𝑨𝒄 = area of concrete
−𝑭𝒚 = yield strength of steel section
−𝑭𝒚𝒓= yield strength of reinforcement
𝒄
−𝒇′ = concrete compressive strength

## Slide 12: Fully Encased Composite Column
AXIAL COMPRESSIVE STRENGTH FEC COLUMNS
Elastic buckling strength
𝑷𝒆 =
𝝅𝟐𝑬𝑰𝒆𝒇𝒇
(𝑲𝑳)𝟐
𝑬𝑰𝒆𝒇𝒇= effective rigidity of composite section
K = effective length factor
L = laterally unbraced length of the member (in)

## Slide 13: Fully Encased Composite Column
AXIAL COMPRESSIVE STRENGTH FEC COLUMNS
Effective rigidity
𝑬𝑰𝒆𝒇𝒇=𝑬𝒔𝑰𝒔 + 𝟎. 𝟓𝑬𝒔𝑰𝒔𝒓 + 𝑪𝟏𝑬𝒄𝑰𝒄
𝑬𝒔= modulus of steel
𝑬𝒄= modulus of concrete
𝑰𝒔= moment of inertia steel section
𝑰𝒔𝒓= moment of inertia reinforcement
𝑰𝒄= moment of inertia concrete
1
𝐶 = 0.1 + 2
𝐴𝑠
𝐴𝑐 + 𝐴𝑠
≤ 0.3

## Slide 14: Fully Encased Composite Column
AXIAL COMPRESSIVE STRENGTH FEC COLUMNS
Nominal compressive strength
𝑷𝒐
If … .
𝑷
𝒆
≤ 𝟐. 𝟐𝟓
𝑷𝒏 = 𝑷𝒐
𝑷𝟎
𝟎. 𝟔𝟓𝟖 𝑷𝒆
𝑷𝒆
Else … . 𝑷𝒐 > 𝟐. 𝟐𝟓
𝑷𝒏= 0.877 𝑷𝒆
The design compressive strength = ∅𝑐𝑝𝑛
Allowable compressive strength = 𝑃𝑛/Ω𝑐

## Slide 15: Fully Encased Composite Column
AXIAL TENSILE STRENGTH FEC COLUMNS
Tensile Strength
Required in situations where uplift is a concern and for
computations related to beam-column interaction.
The design tensile strength. ∅𝑡𝑃𝑛, and allowable tensile strength,
𝑃𝑛/Ω𝑡, for filled composite columns shall be determined for the
limit state of yielding as :
𝑷𝒏 = 𝑨𝒔𝑭𝒚 + 𝑨𝒔𝒓𝑭𝒚𝒓
∅𝒕 = 0.90 (𝐿𝑅𝐹𝐷) Ω𝒕=1.67 (ASD)