## Slide 1
4th Generation Mobile Communications and Beyond

## Slide 2
LTE – Targets
High data rates
  Downlink: >150 Mbps
  Uplink: >50 Mbps
Low delay/latency
  User plane RTT: < 10 ms RAN RTT (fewer nodes, shorter TTI)
  Channel set-up: < 100 ms idle-to-active (fewer nodes, shorter messages, quicker node resp.)
High spectral efficiency
  Targeting 3 X HSPA Rel. 6 (@ 2006 )
Spectrum flexibility
  Operation in a wide-range of spectrum allocations, new and existing
  Wide range of Bandwidth: 1.4, 1.6, 3.0/3.2, 5, 10, 15 and 20 MHz, FDD and TDD
Simplicity – Less signaling, Auto Configuration e-NodeB – ”PnP”, ”Simple as an Apple”
Cost-effective migration from current/future 2/3G systems
State-of-the-art towards 4G
Focus on services from the packet-switched domain

## Slide 3: Simplified Network Architecture
Core NW
SAE Core NW (EPC)
RNC
RNC
NodeB
NodeB
e-NodeB
e-NodeB
WCDMA
LTE/SAE
Moving all RNC functions to e-NodeB
UE
UE
A flat architecture for optimized performance and cost efficiency

## Slide 4
SGSN
Network Architecture
GGSN
Internet
NodeB
IP backbone
HLR
RNC
2G, GSM and GPRS
Duplex techinque: FDD Freq band: 900MHz, 1800MHz, 1900MHz Bandwidth per carrier: 200 kHz Multiple access: TDMA
3G, UMTS with WCDMA
Duplex techinque: FDD (and TDD) Freq band: 2 GHz 15 bands Bandwidth per carrier: 5 MHz BW Access tech: CDMA
BSC
BTS
PDN-GW
MME/ S-GW
MME/ S-GW
eNodeB
eNodeB
IP
LTE/SAE 4G
Duplex technique: FDD or TDD Freq band: 450MHz up to 2.6GHz 15 bands Bandwidth 1.25 – 20 MHz BW Multiple access: OFDM (OFDMA DL and SC-FDMA UL)
VLR
MSC
GMSC
PSTN/ISDN
IMS IP Multimedia subsystem

## Slide 5: E-UTRAN Architecture
eNB
eNB
eN
B
MME
/
S-GW
MME
/S-GW
S1
X2
X2
X2
SAE (Service Architecture
Evolution)
LTE (Long Term Evolution)
EPC (Evolved Packet Core)
E-UTRAN
MME (Mobility Management Entity) | Distribution of paging messages to the eNBs, Security control, Idle state mobility control, SAE bearer control, Ciphering and integrity protection of NAS signalling
S-GW (Serving Gateway) | Termination of U-plane packets for paging reasons; Switching of U-plane for support of UE mobility
eNB (e-NodeB) | RRM: Radio Bearer Control, Admission Control, Connection Mobility Control Scheduling, IP Header Compression, encryption of user data streams, Scheduling and transmission of paging messages, Selection of an MME at UE attachment, Routing of user plane data towards serving GW, Scheduling and transmission of broadcast information, Measurements and reporting

## Slide 6: SAE Bearer Service Architecture
GW
Peer
Entity
UE
eNB
SAE Bearer Service
SAE Radio BS
SAE Access BS
End
-
to
-
end Service
External BS
Radio
Gi
Internet
Phys
.
Radio BS
Physical BS
S
1
E
-
UTRAN
EPC
LTE/SAE

## Slide 7: LTE Physical Layer
Flexible bandwidth
  Possible to deploy in <5 MHz bandwidths up to 20 MHz
Uplink: SC-FDMA with dynamic bandwidth (Pre-coded OFDM)
  Higher power efficiency
  Reduced uplink interference (enables intra-cell orthogonality )
Downlink: Adaptive OFDM
  Channel-dependent scheduling and link adaptation in time and frequency domain
Multi-Antennas, both RBS and terminal
  MIMO, antenna beams, TX- and RX diversity, interference rejection
  High bit rates and high capacity
TX
RX
time
frequency
time
frequency
FDD and TDD concept
  Maximum commonality between FDD and TDD
Minimum UE capability: BW = 20 MHz
10
15
20 MHz
< 5
5
fDL
fUL
FDD-only
fDL
fUL
Half-duplex FDD
fDL/UL
TDD-only
Δf=15kHz
1 ms
180 kHz
User #2 scheduled
User #1 scheduled
User #3 scheduled

## Slide 8
eNB
PD SCH
LTE basics
Category | DL (Mbps) | DL MOD | UL (Mbps) | UL MOD
1 | 10 | 64 QAM | 5 | 16QAM
2 | 50 | 64 QAM | 25 | -
3 | 100 | 64 QAM | 50 | -
4 | 150 | 64 QAM | 50 | -
5 | 300 | 64 QAM | 75 | 64QAM
QPSK
16QAM
Modulation
64QAM
time
freq
PU SCH
Physical Resource Block (PRB): 0.5 ms x 180 kHz
Radio resources
FDD:
TDD:
DL: OFDMA
UL: SC-FDMA
Sharing: frequency & time
UE category
Scheduling: Allocation of Physical resource blocks (PRB) and which Modulation Scheme to use
Alt 1 Round robin, red, black, red
Alt 2 Best quality red, red, red …
Alt 3 Proportional fairness, quality/data volume, red , red , black, red
Also take into account the QoS of the service and UE category
Scheduling
1ms 1ms 1ms
180kHz
Notes: 8
Memory Map: LTE basics
The eNB is responsible for radio resource management. The radio resources to manage are the DL and UL resources either carried on different frequencies (FDD) or on the same frequency (TDD). The bandwidth can range from 1.25 MHz up to 20 MHz, on a range of different frequency spectra (roughly from 450 MHz up to 2.5 GHz). To enable this flexibility and also having a high spectrum efficiency (DL 5 bps/Hz and UL 2.5 bps/Hz) OFDMA has been chosen for the DL. The drawback with OFDMA is the high PAPR, setting high demands on the power amplifier which is a drawback for UEs. For this reason a single carrier type of solution has been selected for the UL, SC-FDMA (also called DFT-spread OFDMA). Sharing is done in both frequency and time, with the minimum resource allocated to an UE at one time is a Physical Resource Block (PRB). A PRB corresponds to 180 kHz x 0.5 ms. For user data and L3 signalling only shared physical channels are used, DL-SCH and UL-SCH.
Scheduling: The process used in eNode B to decide which UE(s) is/are to use which resources (time and frequency, PRB) and with which modulation and coding scheme (MCS). The scheduling process is not specified but open for any implementation. The UE provides the Node B with Channel Quality Inidcator, CQI, indicating the quality on the DL, which may be used for scheduling. Examples of scheduling approaches are: Round Robin, every UE take turns sharing in an equal way in time – advantage: easy, disadvantage: non-efficient from a network perspective; Best quality, the UE with the best quality gets the resource – advantage: efficient use of resources, disadvantage: some UE might not get any resource due to low quality, leading to disappointed subscriber; Proportional fairness, e.g. to provide resources to the UE currently having the highest ratio quality/(received data volume) – advantage: all active UEs gets some data, sooner or later, disadvantage: not the best usage of the resources, but still a good compromise.
MCS: The setting of channel coding and modulation is adjusted to the current radio conditions (influenced by pathloss, interference and fading). 1/3 Turbo coding (3 coded bits generated per data bit) is always used but the amount of puncturing (rate adaptation) can vary so that the effective coding rate varies between 1/3 to 1. Instead of puncturing also bit repetition can be used to provide coding rates of for example 1/4. For modulation QPSK, 16QAM or 64QAM can be used. The current radio conditions for the DL, e.g. C/I, is measured by the UE and reported through CQI sent to eNode B. Decision about MCS is also based on information about UE capabilities.
UE categories: At the moment there are five different UE categories defined based on UE max capabilities.
Category 1: DL 10 Mbps, UL 5 Mbps, 16 QAM, 1 layer for spatial multiplexing
Category 2: DL 50 Mbps, UL 25 Mbps, 2 layers
Category 3: DL 100 Mbps, UL 50 Mbps, 2 layers
Category 4: DL 150 Mbps, UL 50 Mbps
Category 5: DL 300 Mbps, UL 75 Mbps, 64 QAM, 4 layers
CQI: Channel Quality Indicator. Information about radio channel quality based on measurements performed by the UE. CQI is sent to the eNode B. Three types of CQI reporting are currently defined:
Wideband: providing channel quality information of the entire system bandwidth of the cell;
Multi-band: providing channel quality information of subset(s) of the system bandwidth of the cell;
MIMO
Ref. 3GPP 36.300 (E-UTRAN overall description)

## Slide 9: Channel Structure

## Slide 10
Segmentation, ARQ
Ciphering
Header Compr.
Hybrid ARQ
Hybrid ARQ
MAC multiplexing
Antenna and resrouce mapping
Coding + RM
Data modulation
Antenna and resource mapping
Coding
Modulation
Antenna and resource assignment
Modulation scheme
MAC scheduler
Retransmission control
Priority handling, payload selection
Payload selection
RLC #i
PHY
PDCP #i
User #i
User #j
MAC
Concatenation, ARQ
Deciphering
Header Compr.
Hybrid ARQ
Hybrid ARQ
MAC demultiplexing
Antenna and resrouce mapping
Coding + RM
Data modulation
Antenna and resource demapping
Decoding
Demodulation
RLC
PHY
PDCP
MAC
eNodeB
UE
Redundancy version
IP packet
IP packet
SAE bearers
Radio Bearers
Logical Channels
Transport Channel
Physical Channel

## Slide 11: Channel Structure
UL-SCH
PCH
DL-SCH
PCCH
Logical Channels “type of information” (traffic/control)
Transport Channels “how and with what characteristics” (common/shared/mc/bc)
Downlink
Uplink
PDSCH
Physical Channels “bits, symbols, modulation, radio frames etc”
MTCH
MCCH
BCCH
DTCH
DCCH
DTCH
DCCH
CCCH
PRACH
RACH
CCCH
MCH
BCH
PUSCH
PBCH
PCFICH
PUCCH
ACK/NACK CQI Scheduling req.
-Sched TF DL -Sched grant UL -Pwr Ctrl cmd -HARQ info
pri sec
PMCH
PHICH
PDCCH
ACK/NACK
PDCCH info

## Slide 12: Channel Structure
Channel Name | Acronym | Control channel | Traffic channel
Broadcast Control Channel | BCCH | X | 
Paging Control Channel | PCCH | X | 
Common Control Channel | CCCH | X | 
Dedicated Control Channel | DCCH | X | 
Multicast Control Channel | MCCH | X | 
Dedicated Traffic Channel | DTCH |  | X
Multicast Traffic Channel | MTCH |  | X

## Slide 13: Channel Structure
Channel Name | Acronym | Downlink | Uplink
Broadcast Channel | BCH | X | 
Downlink Shared Channel | DL-SCH | X | 
Paging Channel | PCH | X | 
Multicast Channel | MCH | X | 
Uplink Shared Channel | UL-SCH |  | X
Random Access Channel | RACH |  | X

## Slide 14: Channel Structure
Channel Name | Acronym | Downlink | Uplink
Physical downlink shared channel | PDSCH | X | 
Physical broadcast channel | PBCH | X | 
Physical multicast channel | PMCH | X | 
Physical uplink shared channel | PUSCH |  | X
Physical random access channel | PRACH |  | X

## Slide 15: Time-domain Structure

## Slide 16: Time-domain Structure
For TDD, subframe 0 and 5 are always downlink transmissions
  Used for cell search signals and broadcast of system information
Normal CP, 7 OFDM symbols per slot
TCP
Tu  66.7 s
#0
#1
#9
One OFDM symbol
One slot (0.5 ms) = 7 OFDM symbols
One subframe (1 ms) = two slots
One radio frame (10 ms) = 10 subframes

## Slide 17: Guard Time for TDD Operation
Guard time required by TDD provided by DTX of last symbol(s) of the downlink sub-frame preceding the DL-to-UL switch-point
#0
#9
One radio frame (10 ms) = 10 subframes
Normal CP, 7 OFDM symbols per slot
One slot (0.5 ms) = 7 OFDM symbols
One subframe (1 ms) = two slots
Last OFDM symbol(s) not transmitted to create guard time for UL-to-DL switch

## Slide 18: Downlink

## Slide 19: Downlink: OFDM Orthogonal Frequency Division Multiplexing
Benefits
+ Frequency diversity + Robust against ISI + Easy to implement + Flexible BW + Suitable for MIMO + Classic technology (WLAN, ADSL etc)
Drawbacks
Sensitive to doppler and freq errors
Overhead
Orthogonal: all other subcarriers zero at sampling point
Sub carrier spacing 15 kHz
Delay spread << Symbol time < Coherence time
f

## Slide 20: Resource Blocks
The basic TTI (Transmission Time Interval) for DL-SCH is 1 ms
  TTI is a transport channel property
  Subframe is a physical channel property
  One (or two) transport blocks per TTI sent to L1
One resource block is 12 subcarriers during one 0.5 ms slot
f = 15 kHz
One slot (Tslot = 0.5 ms, 7 OFDM symbols)
One resource block
(127 = 84 resource elements)

## Slide 21: DL-SCH Processing
Resource block mapping
Mapping to transmission layers (for multi-layer transmission)
Layer map.
1 transport block per TTI
HARQ
Coding
Scrambling
Modulation
CRC
1 or 2 transport blocks per TTI
Pre-coding (for multi-rank transmission)
Pre- code
HARQ
Coding
Scrambling
Modulation
CRC
CRC insertion (24 bits)
Rel 6 Turbo coding (with QPP interleaver)
Rate matching, redundancy version generation
Scrambling for inter-cell interference randomization
Modulation (QPSK, 16QAM, 64QAM)
Resource block mapping
Resource block mapping
One subframe

## Slide 22: Reference Signals

## Slide 23: Cell-specific Reference Signals
Cell-specific reference signals
  Sequence is a product of
    1 of 3 orthogonal sequences
    1 of 170 pseudo-random sequences
  3170=510 different sequences  510 different cell identities
Used for
  coherent demodulation in the UE
  channel-quality measurements for scheduling
  measurements for mobility
Downlink reference symbol
One slot (0.5 ms)
Time
Frequency

## Slide 24: Cell-specific Reference Signals
One reference signal per antenna port
  1, 2, or 4 antenna ports supported
  specified per antenna port, reference signals are not pre-coded
Different time/frequency resources used for different antenna ports
  Nothing transmitted on ‘other’ antennas when reference symbol transmitted on one antenna
Higher density in time for antenna 1, 2 than antenna 3, 4
Antenna #1
Antenna #2
Antenna #3
Antenna #4
Antenna #1
Antenna #2
Time
Frequency

## Slide 25: Control signaling
Downlink

## Slide 26: Downlink Control Signaling
Downlink control signaling
  DL scheduling (transport format and resource assignment)
  UL scheduling grants
  ACK/NAK related to UL transmission
Transmitted in first n OFDM symbols, n3
  Allows for micro sleep
DL scheduling assignment, UL scheduling grant
  Convolutional coding, QPSK, transmitted over the full BW
One slot (0.5 ms)
One sub-frame (1 ms)
Reference symbols
L1/L2 control

## Slide 27: Cell Search

## Slide 28: Cell Search
Primary and secondary synchronization signal
  Transmitted in subframe #0 and #5
    Primary synchronization signal can be used as phase reference for secondary reference signal
  Uses 62 center subcarriers (~6 resource blocks)  cell search procedure independent of system bandwidth
10 ms radio frame
1 ms subframe
#0
#1
#2
#3
#4
#6
#5
#7
#8
#9
OFDM symbol
Secondary synchronization signal
Primary synchronization signal
0.5 ms slot
0.5 ms slot
0.5 ms slot
0.5 ms slot
0
1
2
3
4
5
6
0
1
2
3
4
5
6
62 subcarriers
0
1
2
3
4
5
6
0
1
2
3
4
5
6
system bandwidth

## Slide 29: Scheduling
Downlink

## Slide 30: Basic DL scheduling mechanism
Ue provides a Channel Quality Report (CQI) based on DL reference symbols
Scheduler assigns resources per RB based on QoS, CQI etc.
Resource allocation is transmitted in connection with data
Many details remain open in 3GPP
CQI report
eNodeB
DL scheduler
Ue
Reference symbols
Resource allocation
Data

## Slide 31: MIMO in E-UTRA DL Shared CH

## Slide 32: Multi Antenna Possibilities
Diversity
“Reduce fading”
  Example
Transmit the signal in all directions
Spatial Multiplexing
“Data Rate multiplication”
  Example
Transmit several signals in different directions
S-P
Delay
Directivity
Antenna/Beamforming gain
  Example
Transmit the signal in the best direction
Channel knowledge (average/instant)
Different techniques make different assumptions on channel knowledge at rx and tx
Many technqiues can realize several benefits
Realized benefit depends on channel (incl. antenna) and interference properties

## Slide 33: Uplink

## Slide 34: Uplink Frequency Hopping
Uplink transmission can hop on slot boundaries
  to obtain channel diversity
  to obtain interference diversity
One sub-frame (1 ms)
1 RB
(12 sub-carriers)
User #1
User #3
User #2
3 RB
(36 sub-carriers)
One sub-frame (1 ms)
User #1
User #3
User #2
No hopping
Hopping

## Slide 35: UL-SCH Processing
UL-SCH processing similar to DL-SCH
HARQ
Coding
Scrambling
Modulation
CRC
CRC insertion (24 bits)
Rel 6 Turbo coding (with QPP interleaver)
Rate matching, redundancy version generation
UE-specific scrambling for interference randomization
Modulation (QPSK, 16QAM, 64QAM)
To DFTS-OFDM modulation, including mapping to assigned frequency resource

## Slide 36: Scheduling
Uplink

## Slide 37: Basic UL scheduling mechanism
Ue request UL transmission via ”scheduling request”
Scheduler assigns initial resources without detailed knowledge of buffer content
More detailed buffer status report follows in connection with data
UL assignments are valid per UE
Ue performs prioritization between RB
Many details remain open in 3GPP
Resource assignment
eNodeB
UL scheduler
Ue
Scheduling Request
Buffer status report
Data
Channel sounding
CQI