## Slide 1: NETWORK PLANNING PROCESS

## Slide 2
The pre-planning process results in theoretical coverage and capacity plans.
The average cell capacity requirement per service area is estimated for each phase of network design.
Coverage-driven to a capacity-driven process.
To find the minimum number of sites for producing the required coverage, radio planners often have to experiment with both coverage and capacity, as the capacity requirements may have to increase the number of sites, resulting in a more effective frequency usage and minimal interference.
Sites are then searched for, and one of these is selected based on the inputs from the transmission planning and installation engineers. Civil engineers are also needed to do a feasibility study of constructing the base station at that site.
Frequency allocation is based on the cell-to-cell channel to interference (C/I) ratio. The frequency plans need to be fine-tuned based on drive test results and network management statistics.
Parameter plans are drawn up for each of the cell sites. This may include cell service area definitions, channel configurations, handover and power control.
The radio plan consists of the coverage plans, capacity estimations, interference plans, power budget calculations, parameter set plans, frequency plans, etc.

## Slide 3: Radio Cell and Wave Propagation
The requirement from the radio planners is generally a network design that covers 100% of the area.
The whole land area is divided into three major classes - urban, suburban and rural - based on human-made structures and natural terrains. The cells (sites) that are constructed in these areas can be classified as outdoor and indoor cells. Outdoor cells can be further classified as macro-cellular, micro-cellular or pico cellular.

## Slide 4: Wave Propagation Effects and Parameters
The signal that is transmitted from the transmitting antenna (BTS/MS) and received by the receiving antenna (MS/BTS)
Free-space Loss
Multi-path propagation
Interference (ISI)
Fading
Refraction
Signal Over Vegetation (Foliage Loss)

## Slide 5: Dimensioning
The dimensioning exercise is to identify the equipment and the network type (i.e. technology employed) required in order to cater for the coverage and quality requirements, apart from seeing that capacity needs are fulfilled for the next few years (generally 3-5 years).
The inputs that are required for the dimensioning include:
The geographical area to be covered
The estimated traffic in each region
Minimum requirements of power in each region and blocking criteria
Path loss
The frequency band to be used and frequency re-use.

## Slide 6: RADIO NETWORK DETAILED PLANNING
The detailed radio network plan can be sub-divided into three sub-plans:
Link budget calculation,
Coverage, capacity planning and spectrum efficiency,
Parameter planning.

## Slide 7
Important Components of Link Budget Calculations
MS sensitivity: This factor is dependent upon the receiver noise and minimum level of Eb/No (i.e. output signal to noise ratio) needed. This is calculated by using the GSM specifications (ETSI GSM recommendation 05.05). The recommended values of MS sensitivity in GSM 900 and 1800 are -102 dBm and -100 dBm respectively.
BTS sensitivity: The sensitivity of the base station is again specified by the ETSI's GSM recommendations 05.05 and is calculated in the same manner as the MS sensitivity. The recommended value of BTS sensitivity is -106 dBm. However, when doing power budget calculations, the value given by the manufacturer (or measured value) should be used.
Fade margin: This is the difference between the received signal and receiver threshold. Usually a fast fade margin is of importance in power budget calculations. Different values are used for different types of regions, such as 2 dB for dense urban or 1 dB for urban.
Connector and cable losses: As cables and connectors are used in power transmission, the losses incurred therein should be taken into account. Cable attenuation figures are usually quoted in loss (dB) per 100 m.
MS and BTS antenna gain: The antennas used for MS and BTS have significantly different gain levels.

## Slide 8: Link Budget & Power Budget

## Slide 9: Link Budget
Link budget calculations give the loss in the signal strength on the path between the mobile station antenna and base station antenna.
Link budget calculations are done for both the uplink and downlink.
Effective Isotropic Effective power

## Slide 10
There is an obvious difference in the results of the uplink and downlink power budget calculations, where the downlink path loss exceeds the uplink power loss. This is an indication that the area covered by the base station antenna radiation is more than the area covered by the mobile station antenna, thereby giving more coverage in the downlink direction. Reducing the power in the downlink direction can reduce this difference but results in a loss of coverage.

## Slide 11: The link budget is the table recording the power loss in the uplink or downlink of the network. Below is an example of the link budget from GSM 900 MHz. The link budget results can be improved by adopting some techniques like frequency hopping or using receiver diversity. (Ref. ETSI)

## Slide 12
The output and effects of link budget calculations:
Path loss and Rx Power: Main output of the link budget. The better the Input data accuracy the more accurate the results.
Cell range: If the path loss is lessened, the signal from the transmitter (BTS) antenna will cover more distance, so increasing the area covered by one BTS. Thus, the power budget calculations play a direct role in determining the covered area, and so deciding on the number of base stations that will be required in a network.
Coverage threshold: The downlink signal strength at the cell border for a given location probability is known the coverage threshold. Although slow fade margin and MS isotropic power can be used to calculate this value, power budget calculations are used for this purpose. Propagation models are used for more accurate calculation of the cell range and coverage area (Cost-hata, Ericsson, SUI).

## Slide 13
Example: Capacity requirements on the Ater interface
Assume, that radio planners have decided that there are five sites of 2 + 2 configuration under a single BSC. Air interface blocking is 2% and Ater 0.1%
5 sites of 2 + 2 configuration = 10 cells, each having 15 TCH
Air interface blocking = 2%
Using Erlang B tables, 15 TCH support = 9.07 Erl of traffic.
Traffic offered to the BSC = 10 x 9.01 = 90.1 Erl.
If Ater blocking probability is 0.1%, then the number of traffic channels supported =117(approx.)
If the number of traffic channels that can be multiplexed on the Ater = 120
Then Ater interface capacity would be = 117/120=0.975 ~ 1 El

## Slide 14
Equipment Location
The base station and TCSM locations need to be decided during the nominal planning phase itself. For Example :If the TCSMs were placed physically near the MSC, it would save transmission costs.
Network Topology

## Slide 15
Site Selection and Line-of-Sight Survey
Transmission planning engineers prefer sites that are very high, so that connectivity to a large number of other sites is possible.
Line-of Sight Survey
Area that is covered by an imaginary ellipsoid drawn between the transmitting and receiving antennas in such as way that the distance covered by the ray being reflected from the surface of the ellipsoid and reaching the receiving antenna is half a wavelength longer than the distance covered by the direct ray travelling from the transmitting to the receiving antennas, i.e.

## Slide 16
Propagation Phenomena
Microwave signal trajectory
Refractivity
Antenna Height
K Factor

## Slide 17
DETAILED TRANSMISSION NETWORK PLANNING
Frequency plan
A microwave link is rarely situated in an isolated environment. There are usually many microwave links in a given region, of the same and/or different network operators. So it is very important to construct correct frequency plans for one's own network.
intra-system interference (noise, imperfections, etc.)
inter-channel interference (adjacent/co-channel, etc.)
inter-hop interference (front-to-back, over-reach)
external interference (other systems, radar, etc.).

## Slide 18
Capacity Planning
Traffic Estimation
Frequency re-use
Avg. Antenna Height

## Slide 19
CORE NETWORK PLANNING PROCESS
It consists of two parts: switch network planning and signaling network planning
Network analysis
Traffic distribution
Apart from voice, this generally includes value-added services such as SMS, MMS, Internet, etc.
Network Dimensioning
Number of switches required to handle subscribers and traffic (both present and forecast)
The most efficient location of the switches in the network
How the switches will be connected to each other (i.e. transmission plan for the switches)
The most efficient way to route the traffic.

## Slide 20
Basics of a Traffic Calculation
Consider a simple core network with one switch.
Subscribers originating (SO): This is the traffic originated by subscribers of the network.
Generally, this input comes from the network (or network operator). Typical values can
be 65% for the switch and/or 50% for the LE.
Subscribers terminating (ST): This is the traffic that is being terminated in the same mobile network. This value can be calculated as ST = 100% - SO.
Own network (terminating) traffic: This is the traffic that is originated in the network and terminated there also. It is usually a product of subscribers in the network and SO.
Loop back of incoming traffic: This is the traffic originating from the external networks and routed back to them.
Outgoing and incoming traffic: Traffic going outside the mobile network to an external network is outgoing traffic, while traffic coming from external networks is incoming traffic.
These can be calculated as follows:
Incoming = (ST- own network traffic)/(I - loop back of incoming traffic)
Outgoing = SO - own network traffic + loop back of incoming traffic.

## Slide 21
Calling and moving interest
Calling interest indicates the distance to which calls are made
Moving interest is another parameter that defines the subscriber behavior of moving within the network.
When the number of subscribers has been determined, the number of switches can be calculated. Thus:
Number of switches = number of subscribers/VLR (or HLR) capacity
transit switch has great importance in this arrangement, it is often advised to have a second redundant transit switch.
If the cellular network is spread over a very large region

## Slide 22
Traffic Dimensioning
There are four MSCs and an external network.
The number of subscribers handled by each MSC is 50,000.
With the traffic generated by each subscriber being 27 mErl (milli-Erlangs), the total traffic generated by each MSC is 1350 Erl.
The percentage of calls originating within their own switch is 60%, of which 40% terminate in the same network.
Calling interest and moving interest are
215 km and 50 km respectively.

## Slide 25
Traffic Estimation
The amount of traffic is expressed in Erlangs, which is the magnitude of telecommunications traffic. An Erlang describes the amount of traffic in one hour :
Erlang=(number of calls in hour)(average call length)/3600 s
Frequency Reuse

## Slide 27
KPIs are more important for GSM radio network optimization & benchmarking to achieve remarkable QoS:
Accessibly
Paging Success Rate
CSSR (Call Set up Success Rate).
CDR (Call Drop Rate).
HSR (Handover Success Rate).
TCH (Traffic Channel) Congestion Rate.