## Slide 1: Path Loss Model in Mobile Cellular Network

## Slide 2
Okumura-Hata Model
Walfish-Ikegami Model
Lee’s Prediction Model

## Slide 3
Microcellular areas span a few Kms.
Okumura in 1968 drew some path-loss curve in the range of 100MHz to 1920 MHz
Masaharu Hata developed empirical path-loss model based on measurement of Okumura known as Okumura-Hata model.
Here separation between BS and MS is greater that 1Km.
Okumura-Hata Model

## Slide 4
Empirical formulation of data provided by the Okumura model and is valid for frequencies in the range 150MHz-1500MHz
For large city,
For small and medium city,

## Slide 5
For suburban and open rural area,
The model is suitable for a distance above 1 Km. The model does not support path specific correction
Coverage
Frequency: 150 MHz to 1500 MHz
Mobile Station Antenna Height: between 1 m and 10 m
Base station Antenna Height: between 30 m and 200 m
Link distance: between 1 km and 20 km.

## Slide 6
Walfish-Ikegami Model

## Slide 7
The Walfish–Ikegami model is an empirical propagation model for an urban area, which is especially applicable for micro cells but can also be used for macro cells.
Model Parameters:
The mean value for street widths (w) is given in metres and the road orientation angle (θ or φ) in degrees. The mean value for building heights (hroof) is an average over the calculation area and is given in metres. The mean value for building separation (b) is calculated from the centre of one building to the centre of another building and is also given in metres.

## Slide 8
Walfish–Ikegami model is suitable for frequencies 800MHz to 2000 MHz where distance can be very small like 200m. Range of BS antenna height 4 to 50m and that of MS is 1 to 3m. Distance in the range of 20m to 5Km.

## Slide 9
For LOS case,
Lm(db) = 42.6 +26log(d) + 20log(fc); d ≥ 20m
For NLOS case, we have to consider,
Hroof = Height of roof-top
ΔhBS = hBS - hroof
ΔhMS = hroof - hMS
w: width of street in meter
b: Building separation in meter along the radio path
φ: Road orientation w.r.t. the direction of radio propagation in degrees incident angle relative to the street).

## Slide 10
NLOS path loss composed of three terms,
LP(DB) = L0 + Lrts + Lmsd
The model works best for the BS much taller than the surrounding buildings.
L0: Free space path loss = 32.4 + 20log(d) + 20log(fc)
Lrts: roof-street diffraction and scatter loss =
-16.9 -10log(w) + 10log(fc) + 20log(Δhm) + Lori
Lori is the street orientation loss:

## Slide 11
Lmsd = multiscreen diffraction loss
= Lbsh+ Ka + Kdlog(d) + Kflog(fc) - 9log(b)

## Slide 12
The parameter Ka increases the path loss in case the BTS is below the rooftop. The parameters Kd and Kf are for adjusting the correction between the distance and frequency with multiscreen diffraction.

## Slide 13
Example:1
Find cell radius for the following parameters.
fc =1800MHz
Street width (w) = 20m
Spacing between buildings (b) = 40m
Average roof height (hroof) = 40m
Mobile antenna height (hm) = 2m
BS antenna height (hb) = 40m
Street orientation φ = 900
Allowable path loss =140dB

## Slide 14
ΔhBS = hBS – hroof = 40 – 40 = 0
ΔhMS = hroof – hMS = 40 – 2 = 38m
Orientation loss,
Lori = 4 - 0.114(φ - 55) = 0.001
Lbsh = -18log(11) + (hBS - hroof) = -18.75dB
Ka = 54
Kf = 4 + 1.5(fc/925 -1) = 5.42
The roof street diffraction and scatter loss,
Lrts = -16.9 -10log(w) + 10log(fc) + 20log(ΔhMS) + Lori
= -16.9 -10log(20) + 10log(1800) + 20log(38) + 0.001
=34.25dB

## Slide 15
Free space path loss,
L0 = 32.4 + 20log(r) + 20log(fc) = 97.5 + 20log(r) dB
Multi screen diffraction loss,
Lmsd = Lbsh+ Ka+ Kflog(fc) - 9log(b) = 38.47 + 18log(r) dB
Allowable path loss,
140 = L0 + Lmsd + Lrts= 97.5 + 20log(r) + 38.47 +18log(r) + 34.25
Or, 38log(r) = -30.23
Or, r = 0.16Km = 160m

## Slide 16: Lee’s Path Loss Model
Lee’s model can be used to predict area-to-area path loss. The
model consists of two parts,
Path loss prediction for a specified set of conditions
Adjustment factors for a set of conditions different from the specified one

## Slide 17
ro = 1mil
= 1,6 km
r
Pro
Pr
Received power,
In (dB),
Lee’s Prediction Model
The model requires two parameters:
Power at 1mile interception Pro in dB.
Path loss exponent γ
n is a constant between 2 and 3 depend on geographical location and operating frequency
is an adjustment factor for different set of conditions

## Slide 18
Carrier frequency, fc = 900MHz
BS antenna height = 30.48 m (100ft)
MS power at the antenna =10W
BS antenna gain = 6dB above dipole gain
MS antenna gain = 0dB above dipole gain
MS antenna height = 3 m (10ft)
Specified conditions

## Slide 19
ao = a1 . a2 . a3 . a4 . a5
Lee’s Prediction Model
α0 in dB,

## Slide 20
There is a 3dB gain received from an actual 4-dB gain antenna at the mobile unit in a suburban area and less than 1-dB gain received from the same antenna in an urban area fro adjusting α5

## Slide 21
Lee’s Prediction Model
Correction factor to determine v in a2
v = 2, for new mobile-unit antenna height > 10 m
v = 1,for new mobile-unit antenna height < 3 m
Terrain | P0γ(dBm) | γ
Free space | -45 | 2
Open area | -49 | 4.35
Suburban area | -61.7 | 3.84
Urban area(New York) | -64 | 4.31
Urban area(Tokyo) | -84 | 3.05
Parameters in Lee’s path loss model

## Slide 22
For suburban area,
Pr = -61.7-38.4log(r) - nlog(f/900) + α0
α0 = 20log(hBS) +10log(Pt) + gBS + gMS +10log(hMS) - 64
Here transmit power in Watt, height of antenna in feet and gain of antenna in dB