## Slide 1: Wet Processing-III Lab
Experiment 05

## Slide 2: Name of the Experiment
Pigment Dyeing of 100% cotton fabric to produce combined shade

## Slide 3: Objectives
To learn about the dyeing process of cotton fabric by pigment.
To learn about the characteristics of pigment, binder & fixer.
To know about the recipe & also the recipe calculation.
To learn about how to utilize the instruments properly.
To know about the combined shade

## Slide 4: Material and Equipment
Sample: 100% cotton knitted pre-treated fabric.
Dyes & Chemicals:
Name of chemicals | Function
Pigment | Coloring Substances to dye the fabric.
Binder | (see theory part)
Fixer | Make Cross Link (see theory part)

## Slide 5: Equipment List:
  Beaker.
  Measuring Cylinder.
  Pipette.
  Pot.
  Tri-pod stand.
  Gas Burner.
  Pot.
  Digital Balance.
  Scissor.

## Slide 6: Working Procedure: (Recipe)
SL | Process Parameter | Unit | Dossing | Stock Solution
01 | Binder | g/L | 1 | 1%
02 | Fixer | g/L | 2 | 1%
03 | Pigment Red | % | 0.5 | 1%
04 | Pigment Yellow | % | 1 | 1%
05 | Pigment Blue | % | 0.5 | 1%
06 | Sample Weight | gm | 5 | ---
07 | M:L | ----- | 1:30 | ---
08 | Temperature | °C | 60 | ---
09 | Time | min | 20 | ----

## Slide 7: Process Curve

## Slide 8: Precautions
  Taking chemicals as per recipe provided by the Instructor.
  Taking every weight of chemicals carefully.
  Switch off the safety system of gas cylinder after complete the experiment.

## Slide 9: Result & Discussion:
Sample Attachment:
Discussion: We observed here the fabric absorbed dyes solution very well.

## Slide 10: Conclusion/Comments
We can say this experiment is successful because our treated fabric absorbed the dye solution & we also observed it bleed very low amount of dyes during hot & cold wash its due to optimum temperature and good quality of pigment and chemicals

## Slide 11: Thank You