## Slide 1: Lecture on Optical Fiber Communication
Presented by:
Sanjida Alam
Lecturer, Dept. of Electrical and Electronic Engineering
Daffodil International University

## Slide 2: Outline of Talk
OF communication system
What is an optical fiber?
Types of optical fiber
How fibers works ?

## Slide 3: Optical fiber communication system
Optical
Transmitter
Comm. Channel
(Optical fiber)
Optical
Receiver
Input
Output
Attenuation, Dispersion, crosstalk & noise

## Slide 4: What is an Optical Fiber?
An optical fiber is a waveguide for light
Consists of :
Core: inner part where wave propagates
Cladding: outer part used to keep wave in core
Buffer : protective coating
Jacket: outer protective shield
SiO2 doped with GeO2
High n
Low n

## Slide 5: Types of fiber optic waveguide
According to the refractive index profile
  Step index fiber
  Graded index fiber
According to the mode of propagation
  Single mode fiber (SM)
  Multimode fiber (MM)

## Slide 6: Basic comparison between SM and MM Fiber
Single mode means the fiber enables one type of light mode to be propagated at a time.
While multimode means the fiber can propagate multiple modes.
The differences between single mode and multimode fiber mainly lies in fiber core diameter, wavelength & light source, bandwidth, color sheath, distance and cost.

## Slide 7: Basic comparison between Step index fiber and Graded Index Fiber
Step index fiber: Refractive index changes sharply.
Graded Index Fiber: Refractive index changes gradually.

## Slide 8: Specification and Performance Ch. of MM step index fiber
Typical structure of MM step index fiber
Refractive index
n1
n2
Structure:
Core diameter : 50 ~ 400 m Cladding dia. : 125 ~ 500 m Buffer jacket dia.:250 ~ 1000 m
NA : 0.16 ~ 0.5
Fiber diameter
Step change in refractive index

## Slide 9: Specification and Performance Ch. of SM step index fiber
Typical structure of SM step index fiber
Structure:
Core diameter : 5 ~ 10 m
Cladding dia. : generally 125 m
Buffer jacket dia.: 250 ~ 1000 m
NA : 0.08 ~ 0.15,
around 0.1
Refractive index
n1
n2
Fiber diameter
Step change in refractive index

## Slide 10: Types of OF with specification and Performance Ch.of MM Graded index Fiber
Typical structure of MM Graded index fiber
Structure:
Core diameter : 30 ~ 100 m
Cladding dia. : 100 ~ 150
Buffer jacket dia.: 250 ~ 1000
NA : 0.2 ~ 0.3
Refractive index
n1
n2
Fiber diameter
Gradual change in refractive ind.

## Slide 11: How Fibers Work

## Slide 12: The General Principle
The classical understanding of fiber optics comes from Snell’s Law!
Step index fibers: Total Internal Reflection
GRIN fibers: layered changes in refractive index

## Slide 13: Total Internal Reflection
i
Exit rays
low index, n2
high index,
n1
c
i
Incident rays
t = 900
According to Snell’s Law
When a ray is incident on the interface between two dielectrics of different refractive indices (e.g. glass-air), reflection and refraction occur.

## Slide 14: Step Index Fiber
n2
n1
i
i
i
i  c for total internal reflection
Cladding
Core
Escapes core (freedom!)
Stuck in core
Escapes from core
c = Critical Angle,
c
n1 > n2

## Slide 15: Graded Index Fiber
n2
n2
n1
n varies Gradually